## Slide 1
  Anne Nisbet
  Health Protection Agency, UK
Progress towards application of ICRP recommendations in the UK: Emergency exposure situations
Notes: <number>

## Slide 2: Scope
Accidents
  Reactors, waste stores, defence sites, transport
Purpose
  Planning for nuclear emergencies
  Response to nuclear emergencies
  Transition to an existing exposure situation
  Long term management of contaminated areas (Recovery)
Notes: <number>

## Slide 3: Current UK emergency advice (1990, 1997)
Emergency Reference levels (ERLs)
Averted dose mSv
Countermeasure Body or organ Lower Upper
Sheltering Whole body 3 30
Evacuation Whole body 30 300
Stable iodine Thyroid 30 300
Notes: The lower ERL is appropriate for circumstances where the disadvantage of implementing the countermeasure is judged to be small (i.e. where few people would be involved, or where implementation had been planned in advance). The upper ERL refers to situations where the disadvantage of implementing the countermeasure is judged to be large (e.g. where many people are involved, or where implementation has not been planned in advance). The upper and lower ERLs are indicative, rather than precise values; they represent ‘a few’, ‘a few tens’, and ‘a few hundreds’ of millisieverts.

## Slide 4: ICRP recommendations (2007, 2008)
Emergency Exposure situations
Reference levels of residual dose should typically be set in the range of 20 - 100 mSv (acute or per year)
  Upper end of range only where protective actions would be very disruptive (e.g. heavily populated area)

## Slide 5: Key issues - UK planning (1)
Are ERLs still applicable?
If so:
Should a two-tier system of ERLs be retained?
Should ERLs be expressed as ‘averted’ or ‘projected’ dose?
Can the current numerical values of the ERLs still be applied?
Then:
How to optimise protection
What role for Reference Levels of residual dose?
Notes: <number>

## Slide 6
How to manage an extended release scenario or prolonged threat phase?
  Extended periods of sheltering or ‘conditional’ sheltering?
  Repeated doses of stable iodine?
How to develop radiological criteria for withdrawal of emergency actions using residual dose?
How to set a dose criterion for normal living above which people would be permanently relocated?
Key issues - UK planning (2)
Notes: <number>

## Slide 7
Willingness to align current UK advice with new ICRP approach
Conceptual thinking
Scoping calculations for a range of reasonably foreseeable worst case scenarios to support the application of the new advice and ensure protection standards are upheld
Engagement with stakeholders on practicability of new advice
Approach to implement ICRP recommendations in UK

## Slide 8: Example findings
1km downwind, on the plume centre line, dry conditions, 100% outdoor occupancy
Contribution of different exposure pathways to projected dose

## Slide 9
Impact of protective actions on residual dose
Example findings

## Slide 10
UK advice likely to include both ERLs and RLs
ERLs
ERLs provide protection in the acute phase
  Site specific action levels still have a role in triggering emergency actions
ERLs assist in protection decisions for larger accidents than those planned for
Two-tier system likely to be retained (flexible and pragmatic)
Some revision of numerical values
Preliminary UK advice (1)

## Slide 11: Preliminary UK advice (2)
Reference Levels
RLs of residual dose are useful criteria to consider when planning an overall response strategy
Residual dose encourages planners to look beyond the emergency phase.

## Slide 12
Optimisation
ERLs with a two-tier approach are already based on generic optimisation
Emergency actions are optimised (in as much as is possible) during planning
There is little time to carry out further optimisation early in the response.
Later on, optimisation of longer term actions is possible
Radiological and other factors will influence the full longer term strategy
Preliminary UK advice (3)

## Slide 13
Stakeholder dialogue will help aid development of advice for longer duration releases (i.e. precautionary evacuation, conditional sheltering and 2nd doses of stable iodine).
RLs have a use in planning for the withdrawal of emergency countermeasures
Preliminary UK advice (4)

## Slide 14: Next steps
HPA consults widely with stakeholders (operators, regulators, local authorities) on practicability of the advice
HPA conducts a public consultation starting Sept 2012.
HPA publishes its new advice in 2013.
This will be the first time the whole spectrum of advice for emergency planning, response and recovery will be presented in a single publication. Advice for CBRN events will follow.
Notes: <number>