## Slide 1: Planned reference and intervention levels in Finland
Raimo Mustonen, STUK
NERIS – ICRP Workshop
6-8 February 2012, Bratislava
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012

## Slide 2: Purpose and procedures
To implement the latest ICRP recommendations (ICRP 103, 109 and 111) into the Finnish authority guidelines
The guidelines drafted by STUK
Process still going on
The guidelines to be issued by the Ministry of Interior
The guidelines separately for early phase and intermediate phase of a radiological emergency
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012

## Slide 3: Protective measures for early phase
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Actions concerning population
Sheltering, partial sheltering
or use of civil defence shelters
Iodine prophylaxis
Access restrictions and
isolation of areas
Evacuation
Protection of workers and other
people in outdoor activities
Foodstuffs and other products
Actions concerning agriculture
Actions concerning raw materials
and production plants
Restrictions and recommendations
concerning trade and use of foodstuffs
and goods

## Slide 4: Protective measures for intermediate phase
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Actions concerning people
Continuation or lifting of sheltering, partial sheltering
or use of civil defence shelters
Control of access
Evacuation
Protection of workers and other
people in outdoor activities
Decontamination of people
Actions on production and living environment
Decontamination of buildings, roads, gardens, residential interiors, vehicles, tools, etc.
Decreasing spreading of radio-
activity in the environment
Restriction of use of land
Business activities in
contaminated areas
Actions on foodstuffs and water
Restrictions on foodstuffs and
drinking water
Restrictions on foodstuff
production and processing, and
use of untreated water
Measures on foodstuff produc- tion and water supply sources
Measures on processing of
foodstuffs and drinking water
Waste containing radioactive substances

## Slide 5: Main approach
20 mSv effective residual dose from all exposure pathways during the first year of an emergency as the reference level
If a projected dose without protective measures during the first year is:
  higher than 10 mSv, it is necessary to perform protective measures; radiation expose is dominant in decision making,
  1 – 10 mSv, protective measures are usually justified but other factors effect decision making,
  below 1 mSv, the protective measures may be carried out especially if they are easily feasible; other factors are dominant in decision making
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012

## Slide 6: Main approach
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Annual
residual
dose,
mSv
Time
Early
phase
Intermediate
phase
Recovery
phase
20

## Slide 7: Categories of contamination levels
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Contamination category | Ambient dose rate (microSv/h) | Strong gamma and beta emitters together (Bq/m2) | Alpha emitters, in detachable form (Bq/m2)
Category I Severly contaminated | > 100 | over 40 000 000 | over 400 000
Category II Heavily contaminated | 10 -100 | 4 000 000 – 40 000 000 | over 40 000 – 400 000
Category III Contaminated | 1 - 10 | 400 000 - 4 000 000 | 4 000 - 40 000
Category IV Moderately contaminated | < 1 | less than 400 000 | less than 4 000
Non-contaminated | on the level of normal background | no contamination at all or very low contamination | no contamination at all or very low contamination

## Slide 8: Dose criteria and operational intervention levels
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Dose criterion (as projected first-year dose)
Ambient dose (equivalent) rate
Airborne concentration (alpha, beta and gamma)
Surface activity (alpha, beta and gamma)

## Slide 9: Dose criteria and operational intervention levels
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Protective action | Dose criteria | Operational intervention level
Sheltering indoors | 10 mSv/2 days | Ambient dose rate 100 µSv/h Concentration in air: alpha emitters 1 Bq/m3 beta emitters 500 Bq/m3 gamma emitters 10 000 Bq/m3 Deposition: alpha emitters 400 000 Bq/m2 strong beta and gamma emitters 40 000 000 Bq/m2
Partial sheltering indoors | 1 – 10 mSv/2 days | Ambient dose rate 10 µSv/h Concentration in air: alpha emitters 0,1 Bq/m3 beta emitters 50 Bq/m3 gamma emitters 1000 Bq/m3 Deposition: alpha emitters 40 000 Bq/m2 strong beta and gamma emitters 4 000 000 Bq/m2
Lifting the sheltering indoors | < 10 mSv/month | Ambient dose rate <10 µSv/h Deposition: alpha emitters <40 000 Bq/m2 strong beta and gamma emitters <4 000 000 Bq/m2
Iodine prophylaxis | 100 mGy to thyroid (adults) 10 mGy to thyroid (children) | Ambient dose rate: 100 µSv/h for adults 10 µSv/h for children I-131 concentration in air: adults 10 000 Bq/m3 children 1000 Bq/m3

## Slide 10: Dose criteria and operational intervention levels
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Protective action | Dose criteria | Operational intervention level
Evacuation | 20 mSv/week | Sheltering indoors lasts over 2 days Ambient dose rate 100 µSv/h Deposition: alpha emitters 400 000 Bq/m2 strong beta and gamma emitters 40 000 000 Bq/m2
Lifting evacuation | < 10mSv/month and decreasing quickly | Ambient dose rate <10 µSv/h and decresing quickly Deposition: alpha emitters <40 000 Bq/m2 strong beta and gamma emitters <4 000 000 Bq/m2
Temporary relocation | 10 mSv/month (Reference level 20 mSv/first year) | Ambient dose rate 10 µSv/h Deposition: alpha emitters 40 000 Bq/m2 strong beta and gamma emitters 4 000 000 Bq/m2
Permanent relocation | 50 mSv/year 1000 mSv in lifetime | Lifetime ambient dose rate 5 µSv/h

## Slide 11: Dose criteria and operational intervention levels
<number>
NERIS - ICRP, Bratislava, 6-8 February 2012
Protective action | Dose criteria | Operational intervention level
Self-decontamination of people |  | Dose rate close to the skin <0.5 µSv/h over the prevailing dose rate at the monitoring place Skin contamination: alpha emitters 0.4 – 100 Bq/cm2 strong beta and gamma emitters 4 – 1000 Bq/cm2
Controlled decontamination of people |  | Dose rate close to the skin >0.5 µSv/h over the prevailing dose rate at the monitoring place Skin contamination: alpha emitters >100 Bq/cm2 strong beta and gamma emitters >1000 Bq/cm2
Sending a contaminated person to hospital |  | Dose rate close to the skin >2 µSv/h over the prevailing dose rate at the monitoring place Skin contamination: alpha emitters >1000 Bq/cm2 strong beta and gamma emitters >10 000 Bq/cm2
Control of access |  | Ambient dose rate >100 µSv/h Deposition: alpha emitters 400 000 Bq/m2 strong beta and gamma emitters 40 000 000 Bq/m2