## Slide 1: A Proposed Countermeasure Simulation Model for the new ICRP recommendations
Claudia Landman and Wolfgang Raskob
Karlsruher Institut für Technologie (KIT)
Institut für Kern- und Energietechnik
 365 days
all values 0
duration and < 365 days
values between scenario

## Slide 2: Decision about new models for ICRP-103 recommendations
In April 2011, the NERIS-TP WP2 group decided about the expansion of RODOS and ARGOS with respect to the new ICRP-103 recommendations. The extension should comprise three components:
  A new screening model that considers all exposure pathways
  The possibility to optimise dose reducing actions with the existing models ERMIN and AGRICP, respectively
  Scenario preparation support tools to help the user in defining countermeasure strategies

## Slide 3: NERIS-TP demands on the screening model
Applicable for nuclear accidents & radiological emergencies
Account for all terrestrial exposure pathways, including ingestion, over some given time period (typically 1 year)
Account for sheltering, evacuation, relocation, iodine prophylaxis, and food restrictions
Screening goal: Define a strategy with above actions for limiting the total effective dose in the given time period below some Reference Level
Long lasting events shall be covered by one run of the atmospheric dispersion model; the generated data shall constitute the basic input for the screening model.

## Slide 4: Key ideas for the proposed SCREEN model
To define an action strategy for limiting the total effective dose in the given time period below a given value, consider separately, but interconnected via the criterion dose
  Sheltering, evacuation and relocation (S/E/R)
  The ingestion pathways
  The intake of stable iodine
With respect to S-E-R, take the "lightest" action first. If this action achieves the goal - reducing the criterion dose value below the RL - the S/E/R problem is "solved". If not, the next "heavier" action is considered, and so on. If none of the actions achieves the goal, the analysis unit gets tagged as a 'residuum' area; there, other actions are required.

## Slide 5: Criterion dose (CD) for S/E/R screening
(+ effective equivalent dose from contamination of skin and clothes) - significant only for very specific scenarios; difficult due to exposure duration
The user can select between 'Open air' and 'normal living'
  Exclude dose mixes in CD (e.g. sum of open air doses for short term exposure and normal living doses for longer term exposure). Although scientifically justifiable, they can lead to inconsistencies and are difficult to transmit to the general public, because they treat different exposure periods under different aspects, and with different aims.

## Slide 6: Determination of areas requiring S/E/R actions
All dose calculations are performed on the basis of the grid cells
The basic analysis unit (BAU) can be 'grid cell' or 'administrative unit' (AU); the latter requires selection whether the 'maximum CD' or the 'mean CD over all grid cells in AU with non-zero contamination' shall represent the administrative unit
Determination of areas requiring S/E/R actions:
  A basic analysis unit where the criterion dose CD representing the BAU exceeds a reference level (RL) gets a 'general S/E/R action required' flag
  A grid cell with the potential for deterministic health effects get a 'DET' flag. To determine such areas, we propose to use a simple model basing on threshold levels to the whole body and individual organs/tissues below which (severe) deterministic effects are not expected.

## Slide 7: Testing for sheltering
The sheltering test area consists of all basic analysis units with the general S/E/R flag
The test looks for basic analysis units where sheltering suffices to reduce the criterion dose below the RL
  Sheltering starts at a general offset time Toffset, or later
    Toffset accounts for situations where doses are already received at some point in time and cannot be mitigated thereafter. Toffset applies to all actions. The user can specify individual starting times for each action, but only for times after Toffset.
  During sheltering, the people are assumed to stay in buildings with shielding properties taken from the geographical data base of the DSS.
    We propose a simple approach with as few factors as agreeable (less uncertainty in the data; easier understanding of results, easier to explain the results to decision makers or the public)
  The maximum shelter duration can be 24 hours, or 48 hours.

## Slide 8: Testing for evacuation/relocation
The evacuation/relocation test area consists of all basic analysis units with the general S/E/R flag where sheltering alone did not reach the goal, and all grid cells with the DET flag
The test looks for basic analysis units where evacuation / relocation, possibly preceded by sheltering, suffices to reduce the criterion dose below the RL, if people stay away from the area for a time period less or equal 365 days
  Proposed "stay out of area" test times: Days in the first two weeks, weeks in the next two months, and thereafter months up to one year, after the start of the accident (no time intervals below 1 day)
  DET: Evacuation/relocation always starts at time Toffset
  S/E/R: Evacuation/relocation starts at time Toffset, or later; for the latter, assume either sheltering or no action exposure in the time span between Toffset and the begin of the action

## Slide 9: 1st main result: S/E/R screening map
 365 days
values between scenario duration and < 365 days
all values 0
all values 0
evacuation/relocation
sheltering
residuum
Boundary of calculation grid
Boundary of area
where CD(no action)  RL
There may be several such areas
numbers in figure <=> "stay-out-of-area times" in days

## Slide 10: 2nd main result: map of doses left for ingestion
0 mSv
dose differences RL - CD(no action)
evacuation/relocation
sheltering
residuum
values in figure: effective equivalent doses
remaining for the ingestion pathways
doses >0 : differences
RL - CD(after S/E/R action)

## Slide 11: Screening model for the ingestion pathways (1)
Aim is to generate an automatic procedure
No intention to assess realistic one year dose distributions for real consumers under consideration of realistic non-local foodstuff production
We propose the consideration of three representative foodstuff classes, and two possible ways to treat them
  Key foodstuffs relevant for home-grown and home-prepared local consumption, for example milk and leafy vegetables
  Drinking water from public water suppliers (not captured rainwater or water from private wells)
  Average annual food basket contaminated just below user specified levels (e.g. permitted EC concentration levels in food), or, alternatively, an user-specified average annual dose value from ingestion.

## Slide 12: Screening model for the ingestion pathways (2)
Approach A: Basically for foodstuffs that can easily be replaced / the consumption can easily be avoided by people in the area (examples: home-grown vegetables, mushrooms)
  Approach A makes uses the effective equivalent doses remaining for the ingestion pathways after S/E/R screening, Dfood
    Dfood sets a limit upon the effective dose value from consumption of foodstuffs in the time span between the stay-out-of-area time and 365 days. The foodstuff screening then consists of calculating whether the consumption of an individual foodstuff during that time span would exceed Dfood in the given grid cell/AU, with respective flagging if it does.
  SCREEN-ING produces maps for each foodstuff where Dfood is exceeded and the corresponding time span, and additionally the potential doses for the foodstuff in that time span

## Slide 13: Screening model for the ingestion pathways (3)
Approach B: Basically for foodstuffs that cannot easily be replaced / the consumption cannot easily be avoided (example: drinking water, measurable but legal contamination level in the foodstuffs available to the all people in the area)
  With approach B, the doses from one or more food stuff are included in the criterion dose for S-E-R screening via the "selected foodstuffs" in the definition of the Criteria Dose.
  During sheltering, evacuation, and relocation, the ingestion of all B-approach ingestion of foodstuffs is assumed to be interrupted, and after a possible return to the area, is continued as if there was no interruption in between.
Additional output of the ingestion model: Maps showing grid cells where the EU CFILs for Baby Food are exceeded for milk

## Slide 14: Screening model for stable iodine intake (1)
Intake of stable iodine difficult to treat consistently in a screening procedure basing on an effective dose criterion
  The criterion for initiating this action up to now is based on the dose to the organ "thyroid", the action effects iodine only.
  For prolonged exposure to radio-iodine, repeated intake of stable iodine would be required to maintain protection.
  Iodine doses to the thyroid from inhalation and ingestion differ significantly between adults and children
  Some countries have an age limit for the measure (e.g. 45 years in Germany), because otherwise the harm to individuals could exceed the benefit to them. This leaves – in one basic analysis unit – part of the population protected, the other part unprotected (for scientifically justified reasons).

## Slide 15: Screening model for stable iodine intake (2)
We propose the following general simplifications
  The iodine test area is defined via a thyroid dose criterion and intervention level
  Intake begins always at time Toffset everywhere in the iodine test area
  Assume repeated intake during long-lasting scenarios
Procedure for children 5 years of age: Carry out two SCREEN-S-E-R assessments, without and with consideration of stable iodine intake, but only for determining all areas where intake of stable iodine suffices to reduce the "no action" CD dose below RL for 5 year old children only, but without testing for the other actions.

## Slide 16: Screening model for stable iodine intake (2)
Procedure for adults: Carry out a separate SCREEN-S-E-R assessment, with consideration of 'intake of stable iodine' as a 'lighter action' than sheltering plus the introduction of a new 'iodine action successful' area flag to indicate the areas where intake of stable iodine suffices to reduce the 'no action' CD dose below the RL, for individuals below a given age only. Please note that this assessment is intentionally made separately and not included in the general screening assessment for adults, because it may apply only to a fraction of the adult population, dependent on the respective national regulations.

## Slide 17: Test cases to demonstrate the completeness
On delivery, SCREEN should be equipped with a set of interesting and not too unrealistic reference scenarios covering typical and extreme situations that can be used for demonstrations as well as for installation and update controls.
The model must be able to cope automatically with the following test cases
  An ingestion-dominated scenario with as little contributions from other exposure pathways as possible
  A pure iodine scenario
  A dirty bomb release with only inhalation-relevant radio-nuclides
  A scenario without any action areas
  A scenario where Toffset is so that no action can achieve any dose reduction

## Slide 18: Documentation
ICRP-103 Screening Model - Functional Specifications - (including ideas about the extensions of ERMIN and AGRICP with respect to optimisation)
  NERIS-TP(WP2)-(11)-01
Scenario preparation support tools to help the user in defining countermeasure strategies
  Proposal for "Radiological Scenario Preparation Assistance" that can be realised in the frame of the existing user interfaces (JRodos: RODOS-Lite), and for "Optimisation Assistance " with ERMIN and AGRICP: NERIS-TP(WP2)-(11)-02

## Slide 19: Thank you for your attention. Questions?