## Slide 1
On the current needs in European decision
support tools for contaminated areas
Kasper G. Andersson
Center for Nuclear Technologies,
Technical University of Denmark (Risø Campus),
DK-4000 Roskilde, Denmark

## Slide 2
Customisation examples for parameters governing dose in RODOS/ARGOS
Time fraction spent outdoors is important: for 662 keV gamma radiation
the kerma rate is often hundreds of times greater outdoors than indoors.
Indoor time fraction estimate used in the past was not based on European
survey.
The Expolis EU project (2004) examined the habits of thousands of people in 7
European cities in detail for use in air pollution studies. Also a few other (older)
European projects have been conducted (with less detail).
In relation to deterministic calculations of dose to the representative person, the
ICRP’s (2007) recommendation for the use of habit data is to use an ‘average value
for the more highly exposed group or 95th percentile of appropriate national or
regional data’. Sufficiently detailed regional datasets to derive 95th percentiles are
only available for the EXPOLIS study.

## Slide 3
 | Time fraction outdoors | Time fraction indoors
Helsinki | 0.73 | 0.27
Athens | 0.74 | 0.26
Basel | 0.73 | 0.27
Grenoble | 0.79 | 0.21
Milan | 0.77 | 0.23
Prague | 0.73 | 0.27
Oxford | 0.75 | 0.25
Average | 0.75 | 0.25
Standard deviation | 0.02 | 0.02
Estimated 95th percentile time fractions spent indoors and outdoors in
various European cities. Average indoor time fraction: 0.89.
Very little variation between cities – no climate trend.
Rural populations might possibly have a different behaviour.
Factors such as age, marital status, working status, education, number of children,
and home environment do not have much influence.
Weekend and season effects even out over long time integration.
American studies show that children (6-12 y) on average spend some 10-20 %
more time outdoors than adults.

## Slide 4
Ventilation rate is important: a fractional increase in ventilation rate can lead to
an increase by the same fraction in dose contributions from inhalation and indoor
surface contamination.
Ventilation rate under natural conditions must be used, as forced ventilation is
assumed to be closed off. Air tightness investigations are generally performed
at elevated pressure. This limits available relevant data.
At high windspeeds ventilation rate increases rather much.
If a window is left open, ventilation rate in the room may increase by a factor of 10.
Based primarily on datasets from 12 European countries, distinction was made
between 3 horizontal bands in Europe: north, central and south, with mean natural
ventilation rates of respectively 0.5, 1.0 and 1.8 ACH.
For the purpose of calculating dose to representative person, 95th percentiles were
calculated. For north, central and south Europe these were respectively 0.9, 1.9
and 3.8 ACH.
Recommended forced ventilation (e.g., for hotel rooms with ensuite bathroom) can exceed 10 ACH (UK).

## Slide 5
Some generic parameterisation needs for the future
Source term is so far generally only considered as a nuclide vector. Important to
consider physicochemical forms of contaminants. The volatility of some
contaminants, e.g., ruthenium, strongly depends on oxidising conditions during
release process. Also inhalation dose needs to consider physicochemical forms.
Post deposition migration: 90Sr dissolved from fuel particles in the areas contaminated by the Chernobyl accident
Deposition velocities and
aerosol sizes

## Slide 6
Source term, including physicochemical forms of contaminants, needs to be
tied to the release process during a power plant accident (e.g., fire, explosion, temperatures, oxidising conditions).
Process-specific parameterisation is also needed for the current decision support tools (RODOS, ARGOS, European handbook for emergency management) to be made applicable for terror scenarios (e.g., RDD’s).
When applied in a ’dirty bomb’, some sources only form large particles, whereas other can be dispersed over a large area. Post-deposition processes in RODOS and ARGOS are based on caesium (highly specific fixation)
Improved modelling of ingestion doses is possible through integration of results of the recent Nordic PARDNOR project (NKS).