## Slide 1: NERIS-ICRP WORKSHOP
EU Basic Safety Standards and European response to the Fukushima accident

## Slide 2: Revision and consolidation of Euratom Basic Safety Standards

## Slide 3: Revision of EU BSS
Article 31 Group of Experts since 2005
Topical issues
  natural radiation sources
  exemption, clearance, graded approach
WP “Recast”
  First consolidated draft text: meeting in June 2009
  Final text for Article 31 Experts in November 2009
Approval of draft text and related Opinion
  on 23-24.2. 2010
Impact Assessment Report
Inter-Service consultation
Translation
Commission proposal adopted in September 2011 (29.9 at 10 am)
http://ec.europa.eu/energy/nuclear/radiation_protection/doc/art31/2010_02_24_draft_euratom_basic_safety_standards_directive.pdf
http://ec.europa.eu/energy/nuclear/radiation_protection/doc/art31/2010_02_24_opinion_on_bss.pdf

## Slide 4: RECAST Better legislation - simplification
Directives:
  Basic Safety Standards (workers, general public): 1996
  Patients/Medical Exposure Directive: 1997
  Informing the public on measures in the event of a radiological emergency: 1989
  Outside Workers: 1990
  High Activity Sealed Sources (HASS): 2003
  (Radon Recommendation 90/143/Euratom)
Recast:
  In principle no discussion of unmodified text
  In practice: too many changes with cross-cutting impact
  Hence: “consolidation”

## Slide 5: Revision of EU-BSS
Consolidation of current Directives
Allow for ICRP/IAEA
  Exposure situations
    rather than processes: practices/interventions
  Incorporate natural radiation sources
    strengthen the requirements
  Protection of the environment

## Slide 6: Reference levels
Bands of reference levels for public exposure and corresponding societal criteria
RL in the range 20 mSv – 100 mSv for emergency exposure situations
  below 20 mSv if no disproportionate detriment or excessive cost of countermeasures
RL in the range 1 to 20 mSv per year for existing exposure situations
  indoor radon exposure
  long-term post-accidental management
RL below 1 mSv for specific pathways of exposure

## Slide 7: Emergency planning and response
More comprehensive system:
  threat analysis
  overall emergency management system
  emergency response plans for identified threats
    reference levels
  pre-planned strategies for the management of each postulated event
Compulsory cooperation between Member States
  Member States shall (instead of …shall seek to)

## Slide 8: Chapter VI: Emergency workers
Responsibility:
  Article 30.1(b): the (emergency response) organisation responsible for the protection of emergency workers
Article 52: Emergency occupational exposure
  Ensure that no emergency worker undertakes actions resulting in doses in excess of 50 mSv
    except in specific cases identified in the national emergency plan
      appropriate reference level above 50 mSv
    In exceptional circumstances, …, a reference level above 100 mSv may be set
  Emergency workers liable to exceed 50 mSv are
    volunteers
    clearly and comprehensively informed, in advance, of the associated health risks and protection measures
  In the event of an emergency exposure:
    radiological monitoring and medical surveillance
    individual dose assessment as appropriate to the circumstances

## Slide 9: Fukushima Impact on Europe and EC Actions: Urgent information exchange (ECURIE)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: EC Reaction: ECURIE
The European Community Urgent Radiological Information Exchange or ECURIE is the Commission’s official framework for informing member states of Radiological Emergencies.
  It was set up by Council Decision 87/600/EURATOM in 1987 in the aftermath of the Chernobyl accident.
  The ECURIE system is managed and operated by DG ENER D4 Radiation Protection Unit in Luxembourg.
  ECURIE is on standby on a 24/7 basis; the officer on duty is prepared to forward any incoming information to Member States within an hour of receipt.
Activated in the morning of 12 March
  3 weeks 24 h active involvement (2-4 people)
    Emergency team for information to other services and cabinets

## Slide 11: Fukushima Impact on Europe and EC Actions: Import controls
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Import controls
Concerns of EU citizens had an adverse effect on the market.
Hence there was an urgent need to ensure harmonised criteria for:
  food and feed,
  ships and containers,
  and other goods.
For this purpose the Commission has issued:
  binding requirements on import checks on food and feed and
  non-binding guidelines for the contamination checks on ships and containers.
The Commission will pursue international standards on permissible levels of contamination of goods, applicable in international trade.

## Slide 13: Regulation 3954/87/Euratom Nuclide categories
isotopes of strontium, notably Sr-90
isotopes of iodine, notably I-131
alpha-emitting isotopes of plutonium and trans-plutonium elements, notably Pu-239, Am-241
All other nuclides of half-life greater than 10 days, notably Cs-134, Cs-137
    C-14 and Tritium not included

## Slide 14: EU maximum permitted levels in foodstuffs (future accident)
° Activity concentration in reconstituted food

## Slide 15: Measures taken by the EC: Food and Feed
Regulation 3954/87 Euratom disproportionate for the import of food from a distant country
On 15 March DG SANCO recommends controls on food imported from Japan
  Maximum levels cf Regulation 3954/87 Euratom
The European Commission subsequently adopted implementing regulations, under general food safety legislation:
  on 25 March with reference to the pre-established maximum permitted levels of radioactivity for different categories of radionuclides laid down in Regulation 3954/87 Euratom,
Action levels in Japan for food and drinking water as well as restrictions on placing on the market of food from affected prefectures and coastal marine produce
  No levels for iodine
  For Cs-137-134: 500 Bq/kg
Commitment from Japan to control export of food on the same basis
  on 11 April (corrigendum on 13.4) amended implementing regulation incorporating the action levels introduced in Japan for iodine and caesium isotopes (as well as plutonium) after the Fukushima accident.

## Slide 16: Measures taken by the EC: Food and Feed
Food products from 12 prefectures in Japan may be presented only with an analytical report on radionuclides Iodine-131 and Caesium-134 +137, by an authorised agency.
  10 % check sampling at import in EU
  20 % monitoring for other prefectures (without certificate)
Recommendation to check marine produce from certain Pacific fishing areas
So far, no contamination found:
  Except, on 15 June: 2 batches of contaminated tea (Roissy, F)
  Up to 31.12.2011: 1967 samples from Japan
    + 409 fish from Pacific
  No iodine
  Caesium detected in around 1% of the samples from Japan
Measures taken by the EC: Food and Feed
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Article 31 Opinion on Food and Feed
Regulation 3954/87 Euratom
  still valid (cf RP 105)
  to be reviewed when new dose coefficients are available
No need to revise Regulation 733/2008/EC (till 2020)
  food imported from countries affected by Chernobyl
Import from Japan
  does not warrant lower levels
  continue checks on the basis of levels in Japan, for as long as needed:
    small volume of import
    moderate levels of radioactivity
    optimisation on the basis of cost of controls and the need to provide reassurance or to allow for consumer preferences
  apply same levels to cosmetics
Basis: likelihood to exceed 1 mSv in a year

## Slide 18
Extension implementing regulation until 31 March 2012
Transition to a long-term regime similar to the one for third countries affected by the Chernobyl accident
  no prescribed minimum sampling frequency
  continued monitoring of the situation in Japan
Gradual relaxation
  no longer checks on radioisotopes of iodine
  revision of the concerned prefectures
  limited categories of food
    green tea
    rice
    fish and fishery products
    mushrooms
    …
  New levels in Japan!
  may be decided upon and implemented on 1 April 2012
Measures taken by the EC: Food and Feed

## Slide 19: Possible lower levels in Japan:

## Slide 20: Food in Japan - Recommendations
Development of a national strategy
  Rational, comprehensive and realistic
  Allow for the low actual dose by food intake
    Reference level 1 mSv
  Avoid low Maximum Permitted Concentrations
    except for basic food (rice, tea)
Chernobyl experience in EU demonstrates
  acceptance of current levels for import
  need for a long-term approach
Involve international stakeholders
  No prejudice to the management of a future accident
    Lowering MPC’s in Japan would be copied by EU for import controls
    Difficult to understand that different levels apply in different situations

## Slide 21: Measures taken by the EC: ships and containers
The European Commission issued on 15 April, through its urgent information exchange tool (ECURIE), an information message to Member States to
  request information on checks for levels of radiation on incoming ships and cargo from Japan,
  proposing harmonised thresholds for further action (decontamination) and reporting:
    threshold: 0.2 µSv/h above background, at 1 m (by default)
    decontamination whenever possible (washing) of any contaminated surface
IMO/ICAO:
  “monitoring of passengers, crew and cargo from Japan carried out to date in other countries, …, does not suggest any health or safety risk. Therefore, screening of radiation … is currently considered unnecessary at airports and seaports around the world.”
Japan (three major harbours):
  checks < 3 x background dose-rate
IAEA: apply international transport regulations
  avoid dispersion of radioactive substance and exposure from fixed radioactivity

## Slide 22: Article 31 Opinion on containers and conveyances
ECURIE criterion good basis for continued screening
Transport Regulations could be understood to apply to conveyances that are not transporting radioactive material
  4 Bq/cm² for β-γ (SCO)
  radiation protection rationale?
  application to emergency exposure situation?
Underline optimisation:
  non-fixed surface contamination to be actually removed whenever practicable
Need for guidance
  definition of non-fixed contamination
  ISO Standard for monitoring methodologies

## Slide 23
no need for continued screening of ships and cargo:
ECURIE information message sent on 19.7:
  reference to Article 31 opinion
  no observed contamination for about one month
  no need for systematic screening
    in line with IMO statement
  request information message in case of future high contamination found to require remedial action
Measures taken by the EC: ships and containers

## Slide 24: Fukushima Impact on Europe and EC Actions: Lessons learned
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: “Stress test”
15 March: Commissioner Oettinger announces stress tests of nuclear facilities in the EU
21 March: Energy Council (energy ministers from MS) endorses the Commission proposal to carry out comprehensive safety and risk assessments
24–25 March: European Council (Heads of State and Government) calls on the Commission and the European Nuclear Safety Regulators’ Group (ENSREG) to develop the scope and modalities of the assessments
24 May: the Commission and ENSREG reach agreement on the methodology and the timetable
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: New legislation
Reflection in parallel to carrying out the stress tests
The Commission interim report indicates the main areas for legislative improvements
3rd quarter of 2012: the Commission will table legislative proposals, taking into account:
  feedback from ongoing public and stakeholder consultation
  technical areas of improvement identified in the stress tests process
  developments in the international nuclear safety legislative regime
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27
EUROPEAN COMMISSION
Brussels, 24.11.2011
COM(2011) 784 final
COMMUNICATION FROM THE COMMISSION
TO THE COUNCIL AND THE
EUROPEAN PARLIAMENT
on the interim report on the comprehensive risk and safety assessments ("stress tests")
of nuclear power plants in the European Union
{SEC(2011) 1395 final}

## Slide 28: Strengthening the EU nuclear safety regulatory framework
The Commission sees scope for improving the legal framework at EU and national level in the following areas:
1) improving technical measures for safety, and improving the necessary oversight to ensure full implementation,
2) improving the governance as well as the legal framework of nuclear safety,
3) improving emergency preparedness and response,
4) reinforcing the EU nuclear liability regime and
5) enhancing scientific and technological competence.
The starting point is the full implementation of existing EU rules
  Basic Safety Standards
  Public information
  ECURIE
  Food
  Civil Protection coordination.

## Slide 29: Enhancing Emergency preparedness and response
Guidelines on national risk assessment
Cross-border nuclear risk management plans
  Enhanced European disaster response
    New BSS: MS’s shall cooperate …
  Site restoration
    New BSS: Criteria for living in contaminated areas
Strengthen information exchange and coordination of responses
  HERCA communication system
  Link with Article 31 Experts and with Health Security Initiative
Food legislation
  Recast of Regulation 3954/87 Euratom
    Delegated powers
    Extension to remote accidents (cf Fukushima)

## Slide 30: Conclusions
Need for thorough reflection on food restrictions
  Nearby and distant events
Need for emergency response plans for circulation of goods
  At local level
    Incident with gravel in Fukushima prefecture
  In international trade
    Revise international transport regulations (surface activities)
    Acceptance criteria for commodities (e.g. code of conduct for metal scrap)
Waste management in emergency situations
EU Harmonisation of emergency response
    Cross-border emergencies
    Trade
    Travel advice
HERCA/EC forum for information exchange on national decisions and communication
Sharing of environmental monitoring data (EURDEP, airborne activity)
Improve risk communication!
Need for:
  New legislation?
  “stress test” of emergency response?