## Slide 1: Activities in Germany related to ICRP 103
Wolfgang Raskob

## Slide 2: Request in 2009
The German Ministry for environment has asked the Commission on Radiological Protection to revise our “Radiological Fundamentals for Decisions on Measures for the Protection of the Population against Accidental Releases of Radionuclides” (Radiologische Grundlagen) from 1999 based on:
  New scientific information (state of the art)
  „Recommendations on the protection of man and the environment against ionising radiation" (ICRP 103)
  UNSCEAR-report „Effects of ionizing radiation" (2006)
  „Basic safety standards for protection against ionizing radiation and for the safety of radiation sources" (IAEA)

## Slide 3: Investigations
One of the key points for discussion is the question if individual measures are consistent with the “residual dose” as defined in ICRP-103
Calculations with RODOS for the following scenarios
  DRSB-F3a (large accident)
  FK2 (very large accident)
  FK5 (long lasting accident)
  FK7 (filtered release)
  CS-137
Areas with dry and wet conditions considered

## Slide 4: Countermeasures
Countermeasures are taken as soon as the criteria is exceeded
sheltering (10 mSv); duration 24 h; Eff. ~ 50%
  Inhalation, external exposure from cloud and ground (7 days)
Evacuation (100 mSv), duration 30 days, Eff. 100%
  Inhalation, external exposure from cloud and ground (7 days)
Temporary relocation, duration 30 days, Eff. 100% from d. 2
  External exposure from ground (30 days)
Permanent relocation, duration 365 days, Eff. 100% from d. 2
  External exposure from ground (365 days)
Iodine blockage and food not considered

## Slide 5: Variation of one potential grid point
Starting point is a map of contamination/dose ranging from a very small value up to very high values
This areal distribution is now converted to a point wise variation of a dose value
Important here to distinguish dry and wet area to have a nuclide vector
Modify that value stepwise (fraction of the initial value) until a criteria is exceeded (number of steps is the entry in the x-axis)
As soon as one single criteria is exceeded, the dose is reduced with the effectiveness defined in the beginning

## Slide 6: DRSB-F3a dry (dose in first year)
Sheltering
Perm. relocation
Evacuation

## Slide 7: FK5 dry (dose in first year)
Sheltering
Temp. relocation
Perm. relocation
Evacuation

## Slide 8: FK5 wet (dose in first year)
Sheltering
Temp. relocation
Perm. relocation
Evacuation

## Slide 9: FK2 dry (dose in first year)
Sheltering
Temp. relocation
Perm. relocation
Evacuation

## Slide 10: Cs-137 dry (dose in first year)
Sheltering
Perm. relocation
Evacuation

## Slide 11: FK7 dry (dose in first year)
Sheltering
Temp. relocation
Perm. relocation
Evacuation

## Slide 12: Summary
Calculations with RODOS for the following scenarios
  DRSB-F3a (large accident)
  FK2 (very large accident)
  FK5 (long lasting accident)
  FK7 (filtered release)
  CS-137
Mostly, the dose in the first year is limited to 100 mSv
  Inhalation is dominant
  Radiation from ground is dominant (wet scenarios)
Only when the dose from inhalation is in between the ground dose from 30 days and 1 year, the dose in the first year may exceed 100 mSv (up to 125 mSv)

## Slide 13
Thank you very much for your attention
Question?