## Slide 1
Jacques Lochard
Chair of ICRP Committee 4
Director of CEPN, France
First NERIS Platform Workshop
“Preparedness for Nuclear and Radiological Emergency Response and Recovery:
Implementation of ICRP Recommendations “
Bratislava, Slovak Republic
6 - 8 February 2012
Notes: <number>

## Slide 2: Content
<number>
    Background
    From ICRP 60 to ICRP 103
      Exposure situations
      Optimization of protection
      Dose constraints and reference levels
    Management of emergency exposure situations
    Transition from an emergency to an existing exposure situation
    Management of existing exposure situations
    Chernobyl experience
Notes: 29/07/26
<number>

## Slide 3: ICRP Publications 103, 109 & 111
<number>

## Slide 4: Earlier guidance for the protection of the public in the event of a nuclear accident
<number>
  ICRP Publication 40 (1984)
    Categorization of accidents in three sequential phases: early, intermediate and recovery phases
    Decisions about applying a countermeasure should balance social costs and the reduction of risk that will result
  Publication 63 (1993)
    Categorization of accidents in three sequential stages: pre-release, release and post-release stages
    Recommendations of quantitative intervention levels for the introduction of protective actions
  Both Publications are giving general principles for planning protective actions mainly during the early and intermediate phases
Notes: 29/07/26
<number>

## Slide 5: Main evolution from ICRP 60 to ICRP 103
No more distinction between practices and interventions. The two concepts are replaced by three generic exposure situations, which cover all conceivable exposure situations:
  planned exposure situations (identical to practices)
  emergency exposure situations
  existing exposure situations
The principles of justification and optimization apply in the same way to the three exposure situations
Dose limits apply only to planned exposure situations
Boundaries exist for optimization as either dose constraints or reference levels
The concepts of action levels and intervention levels are abandoned
<number>
Notes: 29/07/26
<number>

## Slide 6: The three exposure situations (Pub 103, § 176)
Planned exposure situations are situations involving the deliberate introduction and operation of sources
Emergency exposure situations are situations that may occur during the operation of a planned situation, or from a malicious act, or from any unexpected situation, and require urgent actions in order to avoid or reduce undesirable consequences
Existing exposure situations are exposure situations that already exist when a decision on control has to be taken, including prolonged exposure situations after emergencies.
The Commission defines prolonged exposures resulting from nuclear accidents or radiation emergencies as existing exposure situations
<number>
Notes: 29/07/26
<number>

## Slide 7: What is an exposure situation ?
Source
Pathways
Exposed individuals
<number>
Notes: 29/07/26
<number>

## Slide 8: Characteristics of the source and the exposure situations
 | Source
Planned | Deliberately introduced and fully under control
Emergency | Loss of control or unexpectedly introduced
Existing | Already there when decision to control
<number>
Notes: 29/07/26
<number>

## Slide 9: Time factor – Planned exposure situations
Planned from the beginning, and protective actions taken on the basis of planning to prospectively control the source and the pathways
Protective actions can be implemented at any time (to prevent exposure to occur or to mitigate exposure)
Protective actions are effective immediately when implemented
<number>

## Slide 10: Time factor – Emergency exposure situations
Planning can be done for protective actions to be taken to regain control of the source or the pathways
Protective actions must be implemented urgently and in a timely manner to maximize effectiveness
Failure to react means loss of opportunities to reduce exposure
<number>

## Slide 11: Time factor – Existing exposure situations
Planning protective actions can only be done on the basis of a good knowledge of the actual conditions of exposure to control the pathways
Protective actions should not need to be urgent and can be implemented at any time
Protective actions are effective immediately when implemented
Reaching the desired level of protection may take time (e.g. radon and contaminated areas after a nuclear accident).
<number>

## Slide 12: Transitions between exposure situations
Loss of control
of the source
Heritage
of the source
Decision
<number>

## Slide 13: The optimisation principle
Planned exposure situations
(Identical to “practices”)
Dose constraint
Limit
Optimisation
1
1. Added dose
<number>

## Slide 14: The optimisation principle
Reference level
Optimisation
C
C. Added dose
B
A. Averted dose
B. Residual dose
Reference level
Optimisation
Optimisation
A
Mitigation
Prevention
Emergency and existing exposure situations
<number>

## Slide 15: Protection strategy and protective actions
All exposure pathways and all relevant protective actions have to be considered when deciding on the optimum course of action to be taken.
Protection strategy = a set of relevant protective actions
Protective actions are implemented:
  Centrally and locally by authorities, experts, and professionals
  As self-help actions by the affected people themselves with the support of authorities and professionals
<number>

## Slide 16: Rationale for setting dose constraints and reference levels
General objective is to keep exposure below 100 mSv (ICRP 103, § 236)
« At doses higher than 100 mSv, there is an increased likelihood of deterministic effects and a significant risk of cancer. For these reasons, the Commission considers that the maximum value for a reference level is 100 mSv incurred either acutely or in a year. Exposures above 100 mSv incurred either acutely or in a year would be justified only under extreme circumstances, either because the exposure is unavoidable or in exceptional situations such as the saving of life or the prevention of a serious disaster. No other individual or societal benefit would compensate for such high exposures ».
<number>

## Slide 17: Rationale for setting dose constraints and reference levels
According to the characteristics of the exposure situation, including the degree of controllability of the radiation sources, the Commission is recommending a dose scale (corresponding de facto to a risk scale) with three bands: 0 to 1 mSv/year, 1 to 20 mSv/year and 20 to 100 mSv/year, in order to select dose constraints and reference levels
For the protection of the public in case of a nuclear accident the Commission is recommending to select reference levels :
  In the 20–100 mSv/year band for emergency exposure situations
  In the lower part of the 1–20 mSv/year for existing exposure situations, with the objective of reducing exposure below 1 mSv/year in the long term
  Values of reference levels and timeframe will vary from place to place depending on the local circumstances
<number>

## Slide 18: Decisions in emergency exposure situations
Emergency exposure situations correlate to the early and intermediate phases of emergency planning
  Urgent actions include sheltering, evacuation, but also temporary relocation and food ban as mechanisms designed to “quickly” avoid or reduce exposures
  Decontamination is also an urgent action to be implemented wherever it is feasible and effective
  Key decision is whether people must leave, or can stay
<number>

## Slide 19: Permanent relocation
The Commission does not recommend any particular radiation protection criterion
The decision must be taken by the authorities on a case by case basis taking into account the prevailing circumstances i.e. :
  The residual level of exposure in the affected places
  The conditions and means to maintain sustainable societal and economic living conditions of the affected population in these places
<number>

## Slide 20
A good characterization of the radiological situation of the environment, foodstuffs, goods and people
Actions have reduced exposure levels to levels where habitation can be allowed living on an ongoing basis
  Individuals have returned from evacuation and temporary relocation or they are in an area that was never left
An organization of public authorities (national and local) adapted to the situation
The setting up of the conditions and means for the involvement of local authorities and professionals and the local population in decisions and actions for the rehabilitation of living conditions in the affected areas
<number>

## Slide 21: Return from evacuation
The Commission does not recommend any particular radiation protection criterion
Decision to allow return rests with authorities
Consistent with reference levels for existing exposure situations
Ability to provide:
  Protection against potential health consequences
  Sustainable living conditions including respectable lifestyles and livelihoods
Individual choice
<number>

## Slide 22
  Living in a contaminated environment is a complex situation generating a lot of concerns among the affected population
  In the long term ingestion is by far the dominant pathway
  Exposures are driven by individual behaviours and the socio-economic situation
  To be effective protection strategies should include actions implemented by authorities at the national and local levels and by the affected population itself = self help protection actions
  This is the responsibility of authorities to establish programmes for continuous radiation monitoring, health surveillance, information and education of the population
Living in contaminated areas
<number>

## Slide 23: Self-help protection actions
Self help protection action can only be implemented if people understand:
  Where, when and how they are exposed?
  What can be done practically to reduce their exposure?
    - Basis of the radiation protection culture -
Authorities should provide:
  Conditions and means for local monitoring
  General information on the exposure situation
  Information on ways to reduce doses
  Local forums involving the population, professionals and experts
Local monitoring should be focused on:
  Ambient dose rates in living areas
  Concentrations of radionuclides in local foodstuffs
  Internal exposure of people
<number>

## Slide 24: Health surveillance
Authorities should establish a health surveillance program ensuring:
  The follow up of individuals having received significant exposures during the emergency phase
  A general medical monitoring of the population
  The maintenance of health registries for potential epidemiological studies
Authorities should be prepared to modify protection strategy
<number>

## Slide 25: Management of contaminated foodstuffs and other commodities
Long-term restrictions on the consumption of foodstuffs are difficult to maintain and conflicting with the sustainable development of contaminated territories
Authorities should set contamination criteria below or above the Guidelines Level of the Codex Alimentarius according the relative importance of the local foodstuffs in the diet of the population residing in the territories
Need to reconcile the interest of local farmers and the local population with those of consumers and the food distribution sector outside the affected territories
<number>

## Slide 26
Accident: 26 April 1986
Individual dose criteria :
  1986: 100 mSv
  1987: 30 mSv
  1988 and 1989: 25 mSv/year
Proposal in October 1988 of a 350 mSv lifetime projected dose (5 mSv x 70 years) as criterion for allowing permanent residence in the contaminated territories:
  the 350 mSv should include the dose received between April 1986 and December 1989
  the 350 mSv life time projected dose was also proposed for permanent relocation of the population if exceeded
  the proposal should have been applied from January 1990 i.e. 3 years and 8 months after the accident
Chernobyl experience
From the emergency to the existing exposure situation (1)
<number>

## Slide 27
Long debate between the Centre and the Republics, which pushed for a 70 mSv lifetime projected dose as criterion for permanent relocation (1 mSv x 70 years)
Finally republican laws were adopted in the early 90s:
  If the average annual individual dose may exceed 5 mS/year the population must be relocated
  If the average annual dose is ranging from 1 to 5 mSv/year voluntary relocation is possible with compensation = decision of relocation transferred to the individuals
  If the average individual dose is lower than 1 mSv/year periodic radiological control is implemented
From April 1986 to December 1989 the average individual dose over the period was estimated to be around 35 mSv
<number>

## Slide 28
  The involvement of local professionals and inhabitants in the implementation of the protection strategy is key to ensure the effectiveness and sustainability of the rehabilitation programme
  Radiation monitoring in contaminated territories is an unavoidable dimension which is linked to all other dimensions involved in the improvement of living conditions : health, agriculture, social life,...
  The pluralism of sources of measurement (public and private local, regional and national actors) is important for ensuring confidence of the population in the results
  Establishment of places for dialogue is important for the dissemination of information and the development of a common language between all involved stakeholders
Chernobyl experience
Management of the exiting exposure situation
<number>
Notes: <number>

## Slide 29: Summary (1)
Emergency Exposure Situation
Actions driven by urgency
Centralized decision making
Characterization of the radiological situation
Reference levels in the range of 20-100 mSv/year
Existing Exposure Situation
Actions to improve living conditions
Decentralized decision making
Self-help protection
Reference levels in the lower part of 1-20 mSv/year
Management Decision
<number>

## Slide 30: Summary (2)
ICRP Publications 109 and 111 are proposing a flexible framework for guiding actions in case of a nuclear accident or a radiological emergency
The key guidance are to:
  Avoid doses above 100 mSv
  Keep and reduce exposure ALARA all the time
  Engage affected people in the management of the situation
  Develop radiation protection culture among the affected people
  Adopt 1 mSv/year as a long term objective
<number>

## Slide 31
www.icrp.org
Notes: <number>