## Slide 1: An accident scenario for the First NERIS Platform Workshop, February 2012, in Bratislava
Claudia Landman and Wolfgang Raskob
Karlsruher Institut für Technologie (KIT)
Institut für Kern- und Energietechnik

## Slide 2: Contents
Description of accident scenario and consequence assessments with JRodos
Summary of JRodos results prepared for distribution in printed form at the workshop (NERIS-TP(WP2)-(12)-01)

## Slide 3: Accident scenario: Our vision
Generate two contamination patterns in one scenario, separated in space and time:
  One phase should lead to early countermeasures based on classical intervention levels for projected or averted doses, but to an effective dose from all non-ingestion exposure pathways in the first year below 100 mSv
  The other phase one should lead to an approximately homogeneous contamination pattern over a relatively large angular area
  At least one phase should be of longer duration

## Slide 4: Release scenario (1)
Hypothetical accident at fictive nuclear reactor FZK-F at historic location FZK in Germany
  Unit FZK-F represents a pressurized water reactor with 2381 MW thermal power and equilibrium core, stack height = 100 m, and building dimensions 30 x 30 m2.
14. July 13:00 Automatic reactor shutdown due to a severe earthquake in the area
  Some damage of unknown extent at the site. State of block FZK-F uncertain, but pressure is building up.

## Slide 5: Release scenario (2)
15. July 01:00 Planned filtered venting through the stack
  Duration about 1 hour. Release of about 99 % of the initial noble gas inventory (<=> 7 1018 Bq) and 0.1 % of the total initial iodine and aerosol inventory (<=> 9 1015 Bq of Iodine, assumable in elementary form, and 4 1015 Bq of radioactive aerosols).
17. July 02:00 until 31. July 02:00 Uncontrolled releases
  Release of all of the remaining noble gas (<=> 2 1016 Bq), and about 5 % of the initial reactor inventory of iodine and radioactive aerosols (<=> total release in this phase of 8 1016 Bq, of Iodine (elementary form assumed), and 9 1016 Bq of radioactive aerosols).
  Release rate approximately constant over the uncontrolled phase.
  Vertical position of the source(s) unknown; 10 m are assumed.

## Slide 6: Weather sequence (hand-made)
During venting, the wind blows constantly from east-northeast (75 degrees). After the venting, the wind direction changes to a southerly direction (175 degrees).
The "angular homogeneous contamination pattern" was achieved by a daily shift of the wind direction by 10 degrees.
  Although the approach itself does not lead to a realistic weather sequence, the resulting contamination pattern is quite possible for the region.
The effect of rain is demonstrated by one day of mild precipitation (July 26) during the uncontrolled release phase.
During whole scenario, the wind speed is about 3 m/s measured in 10 m above ground; the weather is cloudy and mechanical turbulence prevails (Pasquill-Gifford category D).

## Slide 7: Consequence assessments with JRodos
24 hour prognosis of the situation following an assumed 1 hour venting on July 15, 1:00 o'clock
48 hour prognosis of the situation after start of an assumed constant long duration release, taking into account the situation until July 17, 2:00 o'clock ( a calculation covering 97 hours after July 15, 1:00 o'clock)
As above, but 10 days prognosis duration (covering 241 hours after July 15, 1:00 o'clock, but not yet the day with rain)
Recalculation of whole scenario, from July 15, 1:00 o'clock, until the time when the radioactive cloud has left the area (covering 481 hours after July 15, 1:00 o'clock)

## Slide 8: JRodos : Maps of effective and thyroid doses from non-ingestion pathways
Maps of effective doses [mSv] in 1st year, open air exposure, for 24, 97, 241, 481 hours scenario duration
  Sum of the three pathway doses following below
  Effective dose from cloud gamma exposure over the duration of the scenario episode
  Committed effective dose from inhalation of radioactive material from the cloud over the duration of the scenario episode
  Effective dose from ground gamma exposure in the first year
Maps of committed thyroid doses [mSv] by inhalation of radio-iodine from the cloud over the duration of the scenario episode, open air exposure, for 24, 97, 241, 481 hours scenario duration
  Separately for adults and children

## Slide 9: Example: Map of effective dose [mSv] in 1st year, open air exposure, for 97 hours scenario duration
25 km
10 km
2 km
Exposure pathway sum dose

## Slide 10: JRodos: Time development of effective ground gamma dose (1)
Time plots of effective ground gamma doses in 1st month and in 1st year, at the location of the maximum concentration (from 481 hours scenario)
Example
Time plot
for
1st month

## Slide 11: JRodos: Time development of the effective ground gamma dose (2)
Maps of the effective ground gamma doses [mSv] for open air exposure, for several times after the accident (from 481 hours scenario)
For 1 year after the accident, also a map of the effective ground gamma dose rate [mSv/h] for open air exposure (from 481 hours scenario)

## Slide 12: JRodos: Results for the ingestion pathways, for milk, winter wheat, potatoes (1)
Map of the effective doses [mSv] from the consumption of the foodstuff "ready for consumption" in the first year after the accident, assuming local production and consumption, without restrictions on food marketing or consumption.
Example
Effective
dose
from milk
consumption

## Slide 13: JRodos: Results for the ingestion pathways, for milk, winter wheat, potatoes (2)
Plot of the time development of the effective ingestion dose for the foodstuff, at the location of the maximum dose.

## Slide 14: JRodos: Results for the ingestion pathways, for milk, winter wheat, potatoes (3)
Plot of the time development of the caesium activity concentration in the foodstuff, at the location of the maximum concentration

## Slide 15: JRodos: Potential early countermeasure areas, for 481 hours scenario duration (1)
Maps where the criterion dose [mSv] exceeds the intervention level. As example, German criteria basing on projected doses were used in connection with German intervention levels
  German intervention dose for Evacution:
  Effective dose from cloud gamma exposure*
  + Effective committed dose from inhalation*, for open air exposure
  + Effective dose from ground gamma exposure over at least 7 days**
  * Nominally over the whole cloud passage. Exposure time may be shorter
  in model calculations if the scenario duration is "too short".
  ** The nominal integration time period for groundshine is 7 days. In
  JRodos model EmerSim, the duration is prolonged to the duration of the
  scenario episode for scenarios with a duration exceeding 7 days,
  according to a remark in the German "Radiologische Grundlagen".
  German intervention level: 100 mSv

## Slide 16: JRodos: Potential early countermeasure areas, for 481 hours scenario duration (2)
  German intervention dose for Sheltering is defined as for evacuation, the intervention level is 10 mSv
  German intervention dose for Iodine Tablets
  Thyroid dose [mSv] (committed), resulting from inhalation of radioiodine from the cloud*, for open air exposure, for adults and children
  * Nominally during the whole cloud passage. Exposure time may be shorter in model calculations if the scenario duration is "too short"
  German intervention level for adults: 250 mSv
  German intervention level for children: 50 mSv

## Slide 17: Example: Iodine tablet areas, children, for 481 hours scenario duration
A colour code indicates the day after the start of the scenario when the intervention level for the corresponding action was exceeded for the first time

## Slide 18: JRodos: Potential permanent relocation area, for 481 hours scenario duration
Map of the area where the effective dose from ground exposure in the first year [mSv] exceeds a level of 100 mSv

## Slide 19: Thank you for your attention. Questions?