## Slide 1
Reduction of uncertainty in dose assessment :
Monitoring Approaches
M. Bleher, U. Stöhlker, T. Karhunen, A. Nalbandyan-Schwarz
BfS (Germany), STUK (Finland), DSA (Norway)
D9.7 – Report on uncertainty reduction in exposure assessment based on environmental monitoring data, including concept for identifying critically exposed groups
WP2 Poster P5:
Optimising monitoring in the early phase to reduce uncertainties in dose assessment

## Slide 2: Needs of decision makers
Urgent response phase I - Pre-release
  Potential release (start and duration, radio-nuclides, amount of release)
  Weather conditions (wind direction and velocity, deposition conditions)
Urgent response phase II - Release
  Actual and potential further release (start and duration, radio-nuclides)
  Weather conditions (wind direction and velocity, deposition conditions)
  Monitoring data help to reduce uncertainties about actual situation
Early response phase
  Actual release and weather conditions
  Monitoring data help to reduce uncertainties
    about actual situation (source term)
    affected area
  Combination of prognostic information
  and monitoring data (data assimilation)
  Dose reconstruction methods
  using monitoring data

## Slide 3: Reduction of uncertainties due to monitoring data
RODOS model chain and connected uncertainty budgets and most relevant monitoring data to reduce uncertainties

## Slide 4: Stationary dose rate monitoring
Sources of uncertainties and methods to reduce uncertainties
Probe characterisation
Type testing procedures
Cyclic testing procedures
Inter-comparison experiments
Site characterizing procedures
European data exchange platform EURDEP

## Slide 5: Stationary air monitoring
particulate filter; spectrometry -> nuclide specific activity concentration
particulate filter -> total alpha / total beta activity concentration
Special air filters -> gaseous radioactive iodine concentration
in combination with fallout monitoring and / or in situ gamma spectrometry

## Slide 6: Stationary air monitoring
Monitoring domains and monitoring methods

## Slide 7: Mobile monitoring
Pre-release phase:
Deployable / relocatable dose rate probes
Mobile equipement for air monitoring
to gain additional information during release / cloud passage
Criteria:
Potential affected area
Population density
Example from ERP-Exercise
One from 4 deployable dose rate probes Simulated dose rate for the positions of real probes - November 2019

## Slide 8: Mobile dose rate monitoring
After release phase (Early response phase):
Air-borne dose rate monitoring (e.g. using helicopters)
Car-borne dose rate monitoring
In situ gamma spectrometry and handheld dose rate probes
Criteria:
Population density
Uncertainties from prognostic information and from stationary monitoring
Classification of affected area:
to gain additional information
needed for decisions
for dose assessment

## Slide 9: Mobile dose rate monitoring
After release phase (Early response phase):
Air-borne dose rate monitoring (e.g. using helicopters)
Car-borne dose rate monitoring
in situ gamma spectrometry and handheld dose rate probes
Simulated dose rate for the positions of real car-based probes
Example from ERP-Exercise November 2019
Simulated nuclide specific dose rate for the positions of real in situ spectrometers

## Slide 10: Model results and monitoring data
Combination of prognostic information and monitoring data
assumed source term?
relevant radionuclides?
delineation of affected area?
Urgent protective countermeasures?
Methods of combination:
Simple comparison methods
Data assimilation methods
next presentation
Monitoring data are used
to correct model results
Monitoring data based
dose assessment
Example from ERP-Exercise November 2019

## Slide 11: Optimising monitoring in the early phase
  Results presented in P5!

## Slide 12: External dose-rate measurements based on smartphone CMOS sensor
Objective:
Assess the reliability of dose-rate measurements by the public using smartphone apps
Materials and methods:
  „RadioactivityCounter“ and „GammaPix“
  14 Smartphones in total (from 2017)
  Irradiations with calibrated 137Cs and X-ray sources
Conclusions:
  Better performance of „RadioactivityCounter“ app
  In general, high level of contamination might be identified whereas
  lower or background levels of radioactivity are difficult to assess
  Results presented in P6!

## Slide 13: Outlook and discussion
Combination techniques for prognostic results and monitoring data are needed to reduce uncertainties in decision making process in urgent and early response phase
Data from stationary and mobile monitoring have to be included in tools for the decision making process
Locations probes / air samplers for stationary monitoring should reflect the needs of the decision making process in the urgent and early response phase (properly designed monitoring networks)
Quality assurance techniques for probes, detectors … help to reduce uncertainties
Teams for mobile monitoring need adequate training modules
EP+R exercises
Be confident: Reduction of uncertainty in decision making and dose assessment using monitoring data is possible