## Slide 1
Working Group 2 – Task 2.2
Measurements of Individual Doses
M.A. López1, V. Berkovskyy2, G. Ratia2 , C. Challeton-de-Vathaire3, E. Davesne3, J. Eakins4, D. Franck3, A. Giussani5 , D. Gregoratto4, Hernandez1, U. Kulka5, A. Mafodda6, J.W. Marsh4, J.F. Navarro1, B. Pérez1, I. Sierra1, C. Woda6
1CIEMAT, Madrid, Spain
2RPI, Kyiv, Ukraine
3IRSN, Fontenay-aux-Roses, France
4 PHE, Chilton, United Kingdom
5 BfS, Munich, Germany
6HMGU, Munich, Germany

## Slide 2: Task 2.2 – Measurements of Individual doses (CIEMAT, BfS, HMGU, IRSN, PHE, RPI)
External dosimetry:
Developing destruction free protocols for external dose measurements using electronic components in smartphones
Monte Carlo (MCNP) calculations for organ dose assessment with associated uncertainties
Workshop for integration of biodosimetry into emergency response
Internal dosimetry:
Smartphone/tablet app for the calculation of thyroid dose from monitoring data
Uncertainty evaluation. Sensitivity analysis on thyroid doses.

## Slide 3: External dosimetry using personal items
Objective:
Retrospective dosimetry using personal items to assess individual doses in the lower dose range (20-200 mGy)
Materials and methods:
  Surface mount resistors from mobile phones, readout using TL (Cr3+ emission)
  Chip cards and memory cards, readout using OSL
  Monte Carlo (MCNP) simulations of exposure conditions relevant for NPP accidents for deriving conversion factors from phone to organ doses
Conclusions:
Optimization of measurement protocols and identification of the major sources of uncertainties
Results presented in P8!

## Slide 4: POSTER 8 - External dosimetry using personal items Alessia Mafodda (HMGU, Germany) Clemens Woda (HMGU, Germany) Jon Eakins (PHE, UK)

## Slide 5: External dosimetry- biodosimetry U. Kulka (BfS, Germany)
Biological dosimetry: estimation of the dose of an exposure to ionizing radiation by a biological parameter.
Important tool in cases of radiation accidents.
Workshop for integration of biodosimetry into emergency response - October 2018 (Rovinji, Croatia)
RENEB (European Network of biological and physical-retrospective dosimetry) and the MULTIBIODOSE guidance are able to contribute efficiently to emergency preparedness and response
This needs efforts to consolidate networking and to keep the activities of the partners up to date, efficient and ready.

## Slide 6
  Early phase of the emergency
  Decision on who are the individuals to be monitored: based on information from Task 2.1.
  The intake scenario: acute inhalation of 131I, 132I, 133I, 135I and 132Te
Internal Dosimetry
Improvement on assessment of thyroid doses
(CIEMAT, RPI, IRSN, PHE, BfS)
  (1) Deliverable 2.3: Smart phone/tablet App for direct thyroid dose assessments (M24), RPI-Ukraine
    Use of thyroid monitoring data and dose per thyroid content functions z(t) Gy/Bq for direct assessment of committed absorbed dose to the thyroid.
    New iodine OIR/ICRP Model (ICRP 130/137/ICRP103) for adults; ICRP56/ICRP119/ICRP60 biokinetic and dose coefficients for non-adult population
  (2) Uncertainty evaluation. Sensitivity analysis of thyroid doses.

## Slide 7
EJP-CONCERT
H2020 – 662287
Gennadii Ratia and Volodymyr Berkovskyy , RPI, Kyiv Ukraine
with contributions from: Iurii Bonchuk
D 9.9 - Prototype of processing unit for thyroid dose monitor (IDOSE)
Link to the source code and compiled project of the Prototype of processing unit for thyroid monitoring (CONCERT/CONFIDENCE Deliverable 9.9): https://gitlab.com/GKrok/idose
Compiled project file to be installed to the Android phone is Idose.apk:
https://gitlab.com/GKrok/idose/blob/master/idose.apk
Instructions on how to install .apk file to the Android phone
https://www.wikihow.tech/Install-APK-Files-on-Android
POSTER 7

## Slide 8
The Data Processing Unit (DPU) for Thyroid Monitoring and dose assessment (RPI)
INPUT DATA
Measurement(s) data of activity content in thyroid of 131I and 132I
Date and time of the nuclear accident
Age/date of birth of the person or the gestational age of the foetus.
Results of atmospheric/environmental transport modelling (ATM) with time-course (shape) of the inhalation/ingestion activity intake (Bq) of 131I and 132Te , associated with routes and places visited by the exposed individual;
.
OUTPUT DATA
30-day committed absorbed dose to the thyroid of the exposed person (at term for the foetus) in Gy
Committed absorbed dose to the thyroid at the age of 70y in Gy
Committed effective dose in Sv

## Slide 9
List of exposed persons under investigation
Personal data
Exposed individual
Measurements of 131I and 132I content in the thyroid
Task 2.2: Individual Dose Measurements – Internal dosimetry
IDOSE: Data Processing Unit for Thyroid Monitoring (RPI)

## Slide 10
IDOSE: Data Processing Unit for Thyroid Monitoring (RPI)
Measurements of I-131 and I-132 content (Bq) in the thyroid gland
List of results of monitoring data
Plot of monitoring data vs time
Monitoring data
Date
Activity (kBq)
Uncertainty (%)
MDA (kBq)
Location (Latitude, Longitude)

## Slide 11
IDOSE: Data Processing Unit for Thyroid Monitoring (RPI)
Definition of the general settings of the program and for reviewing of the reference information on the “dose per content” functions
Infant
1-y old child
5-y old child
10-y old child
15-y old child
Adult male
Adult female

## Slide 12
IDOSE: Data Processing Unit for Thyroid Monitoring (RPI)
Dose Assessment - Inhalation
131I and 132I monitoring data
Thyroid absorbed dose (30 d) in Gy
Thyroid absorbed dose (70 y) in Gy.
Effective dose in Sv

## Slide 13
IDOSE: Data Processing Unit for Thyroid Monitoring (RPI)
Dose Assessment – reducing uncertainties:
The use of “Dose per content” function ZI-131 (T,A) ; A= age group
  Directly relates the measured 131I activity content in the thyroid at the time T after the intake MI-131 (Bq) with the committed absorbed dose to the thyroid at the 30th day, from the single acute intake of 131I:
The use of Atmospheric Transport Modelling (ATM) and environmental monitoring data:
  Information on time distribution of concentrations of radioiodines and 132Te in the environment after the accident
  This allows the construction of the Intake shape function
  Correction of the 131I dose in case of intakes of all short-lived radioiodines and 132Te

## Slide 14
The sources of uncertainty:
Uncertainty on the measurement of 131I in the thyroid (M ± 2σ) Bq
Type A and Type B uncertainties: SF = Scattering factor (1.15 - 1.20)
      Nominal value M (Bq) of 131I in the thyroid,
      Upper limit (MxSF2) Bq
      Lower limit (M/SF2) Bq.
SENSITIVITY ANALYSIS on Thyroid doses (CIEMAT, IRSN, PHE, BfS)
Unknown time of the intake (delay between intake and thyroid measurement)
Unknown intake pattern: Acute or Chronic
Not well-defined relative abundance of short-lived radioiodines
Biokinetic and dosimetric models available for dose estimates:
  ICRP119 (ICRP60) for children
  OIR ICRP130/137 (ICRP103) for adults (male/female)
Use of “Dose per per content function”:
insensitive of physico-chemical properties of the incorporated material (e.g. absorption type, AMAD) and to route of intake (inhalation, ingestion) .

## Slide 15
The study may include up to 16 exposure scenarios leading to 16 different dose estimates
Scenario number | Delay between releases beginning and measurements | Intake pattern
1 | 24 h | Acute D0
2 | 24 h | Chronic 24 h
3 | 3 d | Acute D0
4 | 3 d | Chronic 24 h
5 | 3 d | Chronic 3 d
6 | 7d | Acute D0
7 | 7d | Chronic 24 h
8 | 7d | Chronic 7 d
9 | 7d | Acute D0 and J3
10 | 30 d | Acute D0
11 | 30 d | Chronic 24 h
12 | 30 d | Chronic 7 d
13 | 30 d | Chronic 30 d
14 | 30 d | Acute D0 and D3
15 | 30 d | Chronic 7d + Acute D0 and D3
16 | 30 d | Chronic 30 d + Acute D0 and D3
Sensitivity Analysis. Uncertainties in estimation of thyroid doses
D0=Day zero – release
SENSITIVITY ANALYSIS on Thyroid doses (CIEMAT, IRSN, PHE, BfS)

## Slide 16
Thyroid dose-per-content z(t) (accounts of thyroid retention and dose coefficient)
Inhalation – Adult ICRP56/119 (ICRP60) vs ICRP130/137 (OIR, ICRP103) - PHE

## Slide 17
  Real contamination cases - LOW DOSES
EURADOS Survey (Lopez 2016), Europeans exposed in Japan, after Fukushima NPP accident
  Artifitial cases - HIGH DOSES
SENSITIVITY ANALYSIS on Thyroid doses (CIEMAT , IRSN, PHE, BfS)
Objective: “upper level” thyroid dose “lower level” thyroid dose.
Route of intake: Inhalation
Radionuclides: aerosol form (type F) with AMAD = 1 μm.
Different intake scenarios: Acute vs chronic
Different delay from start of release to measurement time

## Slide 18
Real case Study. Single monitoring data. LOW DOSE - Fukushima
Adult male, rescue worker in Ibaraki +Sendai prefecture, 20-28 March 2011
Location and time of Exposure are known
Tokyo 19-20 March 2011;
Mito (Ibaraki) 20-21 March 2011;
Sendai 23-28 March 2011;
Tokyo 28-31 March (then he left to Czecq Republic).
Thyroid monitoring on 6 April 2011 in Prague
M= 52.0 ± 9.0 (2) Bq 131I in thyroid (single monitoring)
Intake:
Inhalation 131I type F , AMAD=1µm. Acute vs Chronic
Releases beginning: 11 March 2011 (Fukushima Daiichi NPP accident)
Exposure in Japan: 19-31 March 2011
Dose assessments: Different intake scenarios and doses (see next table)
  Lower level: 24h chronic intake 31/3/2011 in Tokyo – Hthy = 1.26E-4 Sv
  Upper level: acute intake 20/3/2011 in Mito (Ibaraki) – Hthy= 3.72E-4 Sv

## Slide 19
CIEMAT Case Study. Sensitivity analysis
Rescue worker from Czech Rep. Exposure in Japan: 19-31 March 2011 Thyroid monitoring on 6 April 2011 in Prague

## Slide 20
Artificial case (IRSN) – HIGH DOSES
Female member of the public, 20 years old
Inhalation of I-131 type F, AMAD=1 m.
Multiple monitoring data resulting in high thyroid doses
M1=1.6E+4Bq +/- 320 Bq 131I (7 days after start exposure) D7
M2= 1.0E+4Bq +/- 200Bq 131I (8 days) D8
M3= 8.0E+4Bq +/- 160 Bq 131I (15 days after start exposure) D15
UNCERTAINTIES on the Dose assessment:
Total Uncertainty associated to monitoring data: SF = 1.15 (EURADOS, 2013)
Uncertainty on the intake pattern: (1) acute inhalation at D0 and
(2) chronic inhalation during 7 days
- Contribution to the thyroid dose of radionuclides other than I-131
SENSITIVITY ANALYSIS on Thyroid doses (CIEMAT , IRSN, PHE, BfS)
DOSE ASSESSMENT (ICRP56/119/ICRP60)
22.2 mSv = Hthyr – Lower value
106.6 mSv=Hthy - Upper value (correction for short-lived radionuclides other than 131I)

## Slide 21
CONCLUSIONS
CONFIDENCE WP2/Task 2.2 deals with the integration of dose results for external and internal exposures in an emergency situation
Retrospective dosimetry developments for individual dose assessments:
The use of electronic components of irradiated smart phones (> 20 mGy)
Biodosimetry methods integrated in the emergency response
Thyroid monitoring – Smart phone/tablet App developed by RPI for a rapid evaluation of committed absorbed doses in the thyroid
  Sources of uncertainties on thyroid doses. Sensitivity study:
    “Dose per content function”: insensitive to physico-chemical properties of incorporated material and route of intake when time of measurement > 1 day after start of the radioactive release
    Most relevant uncertainty sources:
      Monitoring data M(Bq) ; SF1.20 (MxSF2 , M/SF2)
      delay of the measurement time with the beginning of exposure
      pattern of the intake (acute vs chronic)
      Contribution of short-lived radioiodines and Te

## Slide 22
Sensitivity analysis AND RAPId ASSESSMENT toolS FOR thyroid doses in a nuclear emergency: AN outcome of the EC CONFIDENCE Project
M.A. López, V. Berkovskyy, C. Challeton-de-Vathaire, E. Davesne, D. Franck, A. Giussani, F. Gering, D. Gregoratto, J.W. Marsh, G. Ratia, L. Walsh, A. Ulanowski, C. Woda
Presentation at IM2020: Work of WP2 /Task 2.2 (internal dosimetry)
and links with Task 2.1 (environmental monitoring) and Task 2.3 (risk assessment)
Report of CONFIDENCE WP2- Task 2.2 – Internal Dosimetry (2019)

## Slide 23
THANKS FOR YOUR ATTENTION