## Slide 1
CONFIDENCE WP2
Scenario facilitated discussion
C. Woda1, T. Hamburger2, M. Bleher2, L. Walsh3
1
2
3

## Slide 2: Part 1: Risk Assessment in the early phase

## Slide 3
Emergency phase – WP1
IAEA 2018 General Safety Guide No. GSG-11
SSK 2014 Radiological Principles for Decisions

## Slide 4: Scenario: Countermeasures based on dose and health risk information
Please consider the following questions while going through the scenario
Which measure would you recommend in which area based on dose information only?
Would consideration of the health risk effects change this recommendation?
Would consideration of the health risk effects change your strategy of evacuation and of distribution of iodine tablets?
Do you find the absolute number of cases in a reference area or the lifetime fractional risk the better quantitity (for decision making and/or risk communication)?
Do you find the health risk information useful?
Would you recommend decision makers to consider the health risk implications?

## Slide 5: Scenario: Countermeasures based on different percentiles of 7d dose
Measures: None Sheltering + ITB Evacuation
Dose*: Any >10 mSv >10 mSv >100 mSv
10th percentile
50th percentile
Devac = 0
Dsh+ITB = 1/3 D (1/10 DTh)
Dnone = D
None Sheltering + ITB Evacuation
Any >10 mSv >10 mSv >100 mSv

## Slide 6: Scenario: Countermeasures based on different percentiles of 7d dose
Measures: None Sheltering + ITB Evacuation
10th percentile
90th percentile
None Sheltering + ITB Evacuation
Devac = 0
Dsh+ITB = 1/3 D (1/10 DTh)
Dnone = D
Dose*: Any >10 mSv >10 mSv >100 mSv
Any >10 mSv >10 mSv >100 mSv

## Slide 7: Variability of possible doses in a given region
Risk (# number of cases) calculated only in the organ dose region from 10 to 500 mGy.
< 10 mGy: uncertainty in risk coefficients too high (any risk?)
> 500 mGy: Onset of deterministic effects for some outcomes. Risk of stochastic effects no longer relevant for decision on countermeasures
Example of a selected RODOS cell

## Slide 8: Dose with health risk information
All solid cancers and leukemia
Measures: None Sheltering + ITB Evacuation
Dose*: Any >10 mSv >10 mSv >100 mSv
10th percentile
No measure
1.6 Million
600.000
33.500

## Slide 9: Dose with health risk information
All solid cancers and leukemia
Measures: None Sheltering + ITB Evacuation
Dose*: Any >10 mSv >10 mSv >100 mSv
10th percentile
LFR = LAR / LBR

## Slide 10: Dose with health risk information
Thyroid cancer
Measures: None Sheltering + ITB Evacuation
Dose*: Any >10 mSv >10 mSv >100 mSv
10th percentile

## Slide 11: Deterministic effects (Basic Radiological Principles, SSK, 2014)
If the absorbed dose exceeds 100mGy, the following organs will display initial functional limitations:
Male gonads (testes): A single dose of around 0.15Gy leads to temporary sterility (permanent > 3Gy)
Female gonads (ovaries): Temporary disorders expected from a dose of around 0.5Gy (permanent ovulation stop at 1 to 2 Gy in >50% of women, complete sterility among all women > 5Gy).
Bone marrow reacts with a measurable disruption to blood cell formation at doses at or > 0.5Gy.
Lens of the eye exhibits a statistically significant increase in the occurrence of clouding at doses > 0.5Gy (latency period - several years or decades)
Animal and human investigations indicate a dose threshold of 100mGy for the induction of anomalies in developing human embryos.
The threshold doses for other tissues and organs are above 1Gy(ICRP 2005).

## Slide 12: Scenario: Countermeasures based on dose and health risk information
Please consider the following points for discussion
Which measure would you recommend in which area based on dose information only?
Would consideration of the health risk effects change this recommendation?
Would consideration of the health risk effects change your strategy of evacuation and of distribution of iodine tablets?
Do you find the absolute number of cases in a reference area or the lifetime fractional risk the better quantitity (for decision making and/or risk communication)?
Do you find the health risk information useful?
Would you recommend decision makers to consider the health risk implications?

## Slide 13: Part 2: Data assimilation: Combining of model results and first monitoring data

## Slide 14: Emergency phase – WP1
IAEA 2018 General Safety Guide No. GSG-11
SSK 2014 Radiological Principles for Decisions

## Slide 15: Emergency phase – WP2
IAEA 2018 General Safety Guide No. GSG-11
SSK 2014 Radiological Principles for Decisions
First monitoring data available

## Slide 16: Data assimilation – Original ensemble
Frequency Plot Effective dose > 10 mSv

## Slide 17: Data assimilation – 1st assimilation step
Frequency Plot Effective dose > 10 mSv
Available positive GDR observations

## Slide 18: Data assimilation – 2nd assimilation step
Frequency Plot Effective dose > 10 mSv
Available positive GDR observations

## Slide 19: Data assimilation Effective dose > 10 mSv
Frequency Plot No data assimilation
Frequency Plot With data assimilation

## Slide 20: Data assimilation Effective dose > 100 mSv
Frequency Plot No data assimilation
Frequency Plot With data assimilation

## Slide 21: Data assimilation Thyroid dose (inh.) > 50 mSv
Frequency Plot No data assimilation
Frequency Plot With data assimilation

## Slide 22: Data assimilation Iodine in milk > 500Bq/kg
Frequency Plot No data assimilation
Frequency Plot With data assimilation

## Slide 23: Part 3: Monitoring approaches Updated combination of model results and monitoring data

## Slide 24: Emergency phase – WP2
IAEA 2018 General Safety Guide No. GSG-11
SSK 2014 Radiological Principles for Decisions
Data from stationary and mobile monitoring available

## Slide 25: Updated combination of model results and monitoring data
Step 1 – Needs for additional mobile monitoring Task 1
Populated area:
Effective dose > IL1 (100 mSv)
Dose rate > OIL1 = 1000 µSv/h
evacuation - relocation?
Effective dose > IL2 (10 mSv)
Dose rate > OIL2 = 100 µSv/h
sheltering - relocation?
Populated area:
Dose rate > OIL3 = 1 µSv/h
improving data base for dose assessment
Data from stationary monitoring
Dose rate µSv/h
Model result after data assimilation:
Effective dose > IL1
(100 mSv)

## Slide 26: Updated combination of model results and monitoring data
Step 1 – Needs for additional mobile monitoring Task 2
Populated area:
Effective dose > IL1 (100 mSv)
Dose rate > OIL1 = 1000 µSv/h
evacuation - relocation?
Effective dose > IL2 (10 mSv)
Dose rate > OIL2 = 100 µSv/h
sheltering - relocation?
Populated area:
Dose rate > OIL3 = 1 µSv/h
improving data base for dose assessment
Data from stationary monitoring
Dose rate µSv/h
Model result after data assimilation:
Effective dose > IL2
(10 mSv)

## Slide 27: Updated combination of model results and monitoring data
Step 1 – Needs for additional mobile monitoring Task 3
Rotterdam
Population: 650 000
Area ~ 350 km2
Effective dose > IL2 (10 mSv)
Dose rate > OIL2 = 100 µSv/h
sheltering?
Data from stationary monitoring
Dose rate µSv/h

## Slide 28: Updated combination of model results and monitoring data
Step 2 – Results using additional information from mobile monitoring Task 1
Data from stationary monitoring
Dose rate µSv/h
Effective dose > IL1 (100 mSv)
Dose rate > OIL1 = 1000 µSv/h
evacuation - relocation?
Identified area for evacuation / relocation:
assessed effective dose from monitoring data using IL1 criteria
Mobile teams
Similar approach for Task2 area

## Slide 29: Updated combination of model results and monitoring data
Step 2 – Results using additional information from mobile monitoring Task 3
Rotterdam
Population: 650 000
Area ~ 350 km2
Effective dose > IL2 (10 mSv)
Dose rate > OIL2 = 100 µSv/h
sheltering?
Data from stationary monitoring
Dose rate µSv/h
Identified area for sheltering using OIL2 criteria
Effective dose
~ 250 mSv
Risk?
Mobile teams

## Slide 30: WP2 - Reduction of uncertainties in dose assessment by combination of data
Individual dose measurements
Health risk assessment
Potentially affected population group
Critically exposed subgroup
Individual dose
identifies
Individualized Dose calculation
Prognosis on dose to population groups
1st Block: Early phase modelling
Optimization, uncertainty budget, data assimilation
Environmental monitoring

## Slide 31: Discussion on monitoring strategies
Please consider the following points for discussion
Which monitoring strategies would you recommend?
Will your strategy be based on prognostic or exsting observation data?
Which areas will be priorised?