## Slide 1
Process-based models for Cs soil-to-plant transfer
Talal Almahayni, Lieve Sweeck, May Van Hees
The Belgian Nuclear Research Centre (SCK•CEN)

## Slide 2: Motivation
Radioecological models are used to predict transfer of radionuclides along the food chain and to make long-term decisions (e.g. planning remediation strategies)
Models must be sufficiently robust, realistic, fit-for-purpose, but not over-parameterised
Existing radioecological models are associated with considerable uncertainties
Notes: FDMT: Food Chain and Dose Transfer Model (a module in JRODOS DSS).
WP3, Task 3.2: ‘Can process based models reduce uncertainties?’
This task will focus on process based models to:
determine why existing process based approaches for Cs gave poor predictions post Fukushima;
investigate the applicability of process based Cs model to European soil types (focusing on soil types not included in model parameterization/validation studies)

## Slide 3: WP3 activities relating to RCs transfer
Assessed applicability to emergency situations of common modelling approaches (focusing on pasture and food crops)
Evaluated the semi-mechanistic approach using novel observations from a range of soils and plants
Identified aspects of the approach that need improvements

## Slide 4
Review of existing RCs transfer modelling approaches

## Slide 5: The empirical approach
Predicts RCs uptake from its average activity concentration in the root zone (top 10 cm for grass and 20 cm for crops).
Advantages:
  Simple
  Practical
Disadvantages:
  Large variability
  Lack of data for none temperate environments
  Lack of data for many crops
Almahayni et al. (2019)
Conc in plant / Conc in soil =

## Slide 6: The semi-mechanistic approach
Predicts RCs uptake from readily available soil parameters
Advantages:
  Uptake is a function of dissolved (bioavailable?) RCs
  Accounts for the “ageing effect”
  Useful to evaluate certain soil countermeasures (K fertilisation)
Disadvantages:
  Developed mainly for Europe
  Under-tested
  Required re-parameterisation for some ‘none European’ conditions
Absalom et al. (2001)

## Slide 7: The semi-mechanistic approach Application to Japanese soils
Uematsu et al. (2015)

## Slide 8: But what is the RIP anyway?
Fuller et al. (2016)
Cremers et al. (1988)
Notes: A small number of highly selective sites [FES] in micaceous minerals control RCs+ sorption in soils.
The RIP is useful for estimating in situ Kd of RCs
e.g., the selective sites contribute ~2% of illite overall CEC.
These sites are present at the edges of the crystal structure of clay particles
Cremers et al. (1988) quantified the abundance and selectivity of those sites using RIP
Fuller et al. (2016) Sorption and incorporation of caesium to sediments and illite clay: a macro to molecular scale investigation. Frontiers in Environmental Radioactivity, London, January 2016.

## Slide 9: The mechanistic approach
Predicts RCs transfer based on biogeochemical behaviour of RCs in soil-plant systems
Advantages:
  Accounts for spatial and temporal distribution of RCs in the root zone
  Accounts for passive and active uptake and (occasionally) competition with K
  Suitable for sensitivity analyses (at processes and parameters levels)
Disadvantages:
  Complex mathematical structure and solution algorithms
  Data intensive
  Some models do not consider K influence on RCs uptake!
  Applicability in emergency situations?

## Slide 10: In summary
Mechanistic
Semi-mechanistic
Empirical
Defensibility
Practicality

## Slide 11: Are existing models fit-for-purpose?

## Slide 12
Evaluation of the semi-mechanistic approach using novel observations

## Slide 13: RCs soil-to-plant transfer experiments
Evaluate the ‘Absalom model’ (an example of the semi-mechanistic approach)
Derive a ‘simpler’ RCs soil-to-plant transfer model

## Slide 14: The study soils
Twenty soils predominantly collected from pastures (N=15)
Country | #Soils | Land use | Soil descriptor
Belgium | 6 | Pasture | C, F, I, J, M, N
UK | 6 | Pasture, Arable | Brimstone, Bromyard, Chiltern, Corney, North Wales, Spark Bridge
Spain | 6 | Pasture, Arable | Bazagona, Casar de Caceres, Monfrague, Retortillo, Torreorgaz, Valero
Norway | 2 | Pasture | R13_14, R15

## Slide 15: Study soils characterisation
The following soil parameters were determined:
pH
Organic matter content (loss on ignition)
Texture (clay, silt and sand content)
Cation exchange capacity (CEC)
Radiocaesium interception potential (RIP)

## Slide 16: Soil parameter variation Arable vs. pasture

## Slide 17: Soil RIP variation Arable vs. pasture

## Slide 18: The study plants Grass, radish and spinach

## Slide 19: TF comparison: WP3 vs. IAEA TRS 472
Notes: WP3 TF stats: 25th, 50th, 75th percentiles and whiskers.
Only summary statistics available from TRS 472 are GM/GSD

## Slide 20: Absalom model evaluation: Predicted grass TF well (for most soils)

## Slide 21: Absalom model evaluation: Predicted TF for radish and spinach ‘reasonably’

## Slide 22: Absalom model evaluation: Under-estimated RIP and over-estimated TF
Notes: Uematsu et al. 2015 found that the Absalom model (all versions) over-estimated the RIP of the Japanese soils by 3 to 10 times.
The model in our test under-estimated the actual RIP of our soils.
Arithmetic mean of Absalom-RIP: 7 cmol/kg
Arithmetic mean of measured RIP: 366 cmol/kg
Measured RIP 50x the estimated RIP.
Geometric mean Absalom-TF based on estimated RIP: 0.036 (3.6E-2)
Geometric mean Absalom-TF based on measured RIP: 0.0006 (6E-4)
Grass TF based on estimated RIP is 60x TF based on measured RIP

## Slide 23: Absalom model evaluation: Any better than an average TF?
Predicting RCs concentration in grass biomass

## Slide 24
Is there a ‘simpler’ transfer model?

## Slide 25: Predicting TF from soil parameters: grass
Coefficient | Value SE. | P value
 | 3.6 1.6 | 0.05
 | -0.4 0.2 | 0.1
 | -0.02 0.01 | 0.1
 | 0.17 | 0.1
Coefficient |  | P value
 |  | 0.05
 |  | 0.1
 |  | 0.1
 | 0.17 | 0.1
Notes: Stepwise multiple regression. Soil parameters included pH, OM content, clay content and CEC.
Number of soils included: 19 (R15 excl. due to lack of clay content data)

## Slide 26: Predicting TF from soil parameters: radish
Coefficient | Value SE. | P value
 | 0.50.2 | 0.01
 | -0.009 0.005 | 0.1
 | 0.11 | 0.1
Coefficient |  | P value
 |  | 0.01
 |  | 0.1
 | 0.11 | 0.1

## Slide 27: Predicting TF from soil parameters: spinach
Coefficient | Value SE. | P value
 | 3.41.8 | 0.05
 | -0.4 0.2 | 0.1
 | -0.017 0.01 | 0.1
 | 0.21 | 0.1
Coefficient |  | P value
 |  | 0.05
 |  | 0.1
 |  | 0.1
 | 0.21 | 0.1

## Slide 28: Conclusions
The semi-mechanistic approach is potentially useful for application following emergency situations to predict long-term RCs transfer to plants (more on this later)
The model of Absalom et al. (2001) is a candidate that is defensible and practical
The ‘default Absalom model’ predicted transfer to grass well and transfer to radish and spinach reasonably
The Absalom model should be parameterised for more soils and plants including non-temperate

## Slide 29: Where to find more details?

## Slide 30: Acknowledgements
Partners who have provided soils and valuable data:
  Belgian Nuclear Research Centre in Mol (SCK-CEN)
  UK CEH
  DSA (Norway)
  University of Extremadura (Spain)