## Slide 1
Developing a process based approach to predicting Sr concentrations in plants
Steve Lofts &
Nick Beresford

## Slide 2: Initial objective
Evaluate the use of a mechanistic, process-based chemical speciation model for predicting Sr soil chemistry
  Assess minimal parameter requirements
  Can outputs be used to model plant concentrations?

## Slide 3: Introduction: chemical speciation modelling
Individual chemical reactions
Sr2+ + CO32- ↔ SrCO3
Sr2+ + OM ↔ Sr-OM
Sr2+ + clay ↔ Sr-clay
System composition
Porewater chemistry:
pH, DOM
Solid phase: major adsorbing components, labile major ions

## Slide 4: Windermere Humic Aqueous Model (WHAM)
Clay
SOM
Humic acid
Fulvic acid
Metal oxides
Solution complexes
DOM
Fulvic acid
Sr2+

## Slide 5: ‘Full’ parameter/variable requirements
Solution
Clay
Specific surface area
Selectivity coefficients
OM
Activity
pH
Labile major ions
Na, Mg, K, Ca
Cl, NO3, SO4
DOM
Labile Al, FeIII
‘Active’ OM content

## Slide 6: Clay model fitting
SSA = 700 m2 g-1
DL volume = 0.005 dm3 g-1
log Ksel, Sr = 0.9
(log Ksel, Na = 0.0)

## Slide 7: Clay model fitting (2)

## Slide 8: Clay model fitting (3)
Need Ksel for Mg, K, Ca
Huertas et al., J. Coll. Int. Sci, 239, 409-416 (2001)
  Na, Mg, K, Ca sorption to same clay
log Ksel, Mg = 0.46
log Ksel, K = 0.9
log Ksel, Ca = 0.62

## Slide 9: Testing dataset
Gil-García et al., Appl. Rad. Isot., 66, 126-138 (2008)
30 soils of Spain
pH 4.3-9.2, Corg (%) 0.2-9.4, clay (%) 6.3-52.4
Soil solution obtained by saturation extraction
  Labile soil cations by back calculation in WHAM
Best fit found by adjusting clay SSA
to 300 m2 g-1

## Slide 10: Example results
SOS in log Kd = 2.18
SOS in log Kd = 1.79
SOS in log Kd = 432
SOS in log Kd = 2.30

## Slide 11: Application to plant media from CEH greenhouse study Clay SSA = 300 m2 g-1, OM 75% of LOI

## Slide 12: Plant study: experiment - overview
Edible food crops & grass grown in a range of soils
Concurrent studies in UK (2018/19) & Spain 2018
Soil: Bought from commercial supplier or collected from field sites (UK and Spain)
Crops: Grown to maturity in greenhouse or outside
Irrigation & pore waters: Water used for watering and pore waters were extracted from soil (using rhizons)

## Slide 13: Soil characteristics
Soil | pH | LOI (%) | % clay | % sand
Heath (UK, commercial) | 4.9±0.4 | 13.5±1.1 | 2.7±1.0 | 84±5.2
Top (UK, commercial) | 7.3±0.2 | 3.5±0.3 | 8.6±0.3 | 60±1.4
Loamy sand (UK, Nottingham) | 7.0±0.3 | 3.4±0.1 | 8.1±0.3 | 79±1.1
Clay loam (UK, Nottingham) | 7.5±0.4 | 4.9±0.3 | 18±1.8 | 49±4.9
Spark Bridge (UK, Cumbria) | 6.2±0.3 | 21±1.5 | 16±0.1 | 40±0.4
Casar de Caceres (Extremadura) | 7.0±0.6 | 5.5±2.2 | 7.9±0.3 | 53±1.3

## Slide 14
Strawberries were grown in UK in Spanish soil due to export restrictions
CROPS
Grass (prior to flowering)
Lettuce
Courgette (fruits)
Potato (tuber flesh and peel)
Chard
Radish (leaf and bulb)
Strawberry (leaf and berry)

## Slide 15: Analysis - overview
Soil
  Total and exchangeable Ca, Cs, K, Mg & Sr concentrations by ICP-MS analysis (aqua regia & BaCl2 extraction)
  NH4-N concentration
Crops and grass
  Ca, Cs, K, Mg & Sr concentrations
Irrigation and pore water
  Ca, Cs, K, Mg, Sr & Ti concentrations by ICP-MS analysis
  Total organic carbon (TOC) concentration
Barnett, C.L., et al. (submitted) Elemental concentrations (Ca, Cs, K, Mg, Sr) in a range of crops and associated soils. NERC-Environ. Inf. Data Cent.

## Slide 16: Soil concentrations mg/kg DM
Soil | Ca | Sr | Mg
Heath (UK, commercial) | 2380 | 7.0 | 260
Top (UK, commercial) | 3990 | 10.0 | 730
Loamy sand (UK, Nottingham) | 2690 | 4.8 | 2390
Clay loam (UK, Nottingham) | 6200 | 13 | 12400
Spark Bridge (UK, Cumbria) | 13600 | 59 | 6610
Casar de Caceres (Extremadura) | 3500 | 22 | 1560

## Slide 17: Crops Sr v’s Ca

## Slide 18: Max to Min of different CRs (calculated from data)

## Slide 19: Observed ratio (OR)
OR is approx. unity for plants
This study
 | Soil | Pore water
Mean | 0.88 | 0.96
GM | 0.82 | 0.91

## Slide 22
Chaplow, J. et al. (submitted) Calcium and magnesium concentrations in plants used as human and animal foods derived from global literature. NERC-Environ. Inf. Data Cent. (>2000 records)

## Slide 23
Measured – Predicted (‘OR model’)

## Slide 24
Measured – Predicted (TRS472 CRs)

## Slide 26
Measured – Predicted
(‘WHAM model’ + OR)

## Slide 27
Simplified WHAM model gives ability to make predictions of plant concentrations based on limited number of soil parameters
Simple plant Ca concentration & OR model gives reasonable predictions
Conclusions

## Slide 28
Simplified WHAM model gives ability to make predictions of plant concentrations based on limited number of soil parameters
Simple plant Ca concentration & OR model gives reasonable predictions
Predictions better than conventional CR approach
(Should) Work for any crop in Ca database
Conclusions

## Slide 29
Need to test against data for wider range of soils and crops
Currently – equilibrium predictions. Can we make dynamic?
Does considering Mg concentration in plants improve predictions?
Improve pore water predictions for WHAM adaptation
To do

## Slide 30
Any Questions?