## Slide 1
ECOLEGO implementation of models
FDMT, Absalom and Hot particle
Ali Hosseini & Justin Brown
Norwegian Radiation and Nuclear safety Authority (DSA)

## Slide 2: FDMT
The FDMT (Food Chain and Dose Module for Terrestrial Pathways) software has been implemented in both RODOS and ARGOS.
The methods applied to simulate the transfer of radionuclides in food chains are essentially those of the radioecological model ECOSYS-87 (Müller & Pröhl 1993).
The module allows for the prediction of
  radionuclide activity concentrations in various, mainly agricultural, food products for given inputs of radionuclides into geographically-defined terrestrial systems.
  doses to members of the public via relevant pathways including internal exposure (from ingestion and inhalation) and external exposure (from plume passage and deposited radionuclides).
Müller, H., Pröhl, G. (1993). ECOSYS-87: a dynamic model for assessing radiological consequences of nuclear accidents. Health Phys., 64 (1993), pp. 232–252

## Slide 3: FDMT: inputs and structure
  the date of the deposition (day, month)
  the time-integrated radionuclide activity concentration in near ground air
  the activity deposited by precipitation per unit ground area
  the amount of precipitation if wet deposition has occurred
Starting from these input data, the transfer of radionuclides through food chains is quantified by modelling various processes.

## Slide 4: FDMT within ECOLEGO - Background
Rationale:
  ECOSYS-87 is in an Excel format and FDMT is an integrated part of the ARGOS and RODOS systems
  Parameter manipulations and model runs can be cumbersome
  Option to conduct sensitivity/uncertainty analyses
Transferring to ECOLEGO provides us with the flexibility to:
  Explore the implications of updating parameters taking into account international recommendations (i.e. IAEA Technical Report Series 472)
  Adopt region specific parameters and including the underlying parameter variability (undertaking probabilistic simulations)
  Consider alternatives to the current model set-ups, e.g. replace analytically based food-chain transfer models with compartmental models

## Slide 5: What is ECOLEGO?
Modelling platform for creating dynamic models and performing deterministic or probabilistic simulations.
Powerful numerical solvers for complex and dynamic systems, i.e. solver for ordinary differential equations including ‘stiff’ problems.
ECOLEGO player:
Ecolego Player is a free software for distributing Ecolego models.
Review model structure and equations.
Run probabilistic simulations
http://ecolego.facilia.se/ecolego/show/Software

## Slide 6: ECOSYS-87/FDMT in ECOLEGO

## Slide 7: Model testing
Scenarios were devised to test the implementation;
Comparisons of model runs provided good match;
Confident that ECOSYS-87 has been implemented correctly.

## Slide 8: Data collation enabling probabilistic model runs
Populate FDMT-ECOLEGO with DEFAULT values, statistics (mean, s.d.) and distributions.
Narrowed scope to look at food-chain transfer only.
Initial focus has been on radiologically important nuclides Cs-137 (Cs-134), Sr-90 and I-131.
Main focus on radionuclide dependent parameters (e.g. soil to plant transfer factors, transfer coefficient (d kg-1) for animal product).
However, radionuclide-independent parameters (such as plant growing and harvesting times, animal feeding characteristics) are known to be regionally important.
Intention has been to define stats/distributions for identified parameters but many of these do not have empirically defined distributions.

## Slide 9: Sensitivity analyses in ECOLEGO
1) Graphical methods: Analysis of scatter plots of inputs versus outputs
2) Screening methods: which parameters have the highest effect, using the Morris method
3) Linear regression and correlation methods
4) Variance-based methods

## Slide 10: Structural changes to FDMT-ECOLEGO and introduction of libraries
Sources – essentially for defining the input from atmospheric dispersion modelling
Receptors – blocks, such as intensive grass-land, receiving radionuclide deposition
Processing and storage of different food- and feedstuff – for defining parameters related to this category
An initial structural change to the model is to differentiate between:
Dose calculation – where the configuration for human dose calculations can be performed.

## Slide 11
Advantages:
users can select specifically what they are interested in without invoking the entire FDMT model;
  Reduces the risk of introducing error when adding/replacing models.
Facilitates flexibility,
  New model components can be replaced and tested much more simply.
FDMT-ECOLEGO: library structure

## Slide 12
The structure within each library block has now been changed:
Soil is separated from vegetation
Independent ‘soil model’ block
Different soil models can be tested by removing the old and ‘plugging in’ the new.

## Slide 13: Absalom model implementation in ECOLEGO
Version implemented = Absalom 2001 as described in Tarsitano et al. (2011).
Model tested against EXCEL (Absalom) version and results agree closely.
We can use the model to provide 137Cs activity concentrations in plants with time.
Tarsitano et al. (2011). Evaluating and reducing a model of radiocaesium soil-plant uptake. Journal of Environmental Radioactivity, 102 (3), pp. 262-269

## Slide 14
The distribution of radionuclides in soil systems with respect to potential different physico-chemical forms of radioactive fallout, and uptake by plants.
Fixed
New soil model: including hot particles
A0
A1
A2

## Slide 15: New soil model
New model has been set up within ECOLEGO.
3 compartments representing 3 fuel particle (FP) categories: U-Zr-Oxides, UO2 and UO2+x.
Each fuel particle type has a specific weathering rate that changes as a function of pH.

## Slide 16: Model testing
Scenarios were developed to be compatible with empirical data for Ukrainian soil and grain 2011-2018. This required:
Representative soil parameters with rate constants defined for podzoluvisols
Fraction of aerosol and FP types for various pH conditions (low, medium and high)
Models were run for a deposition to soil of 1 kBq/m2 of 137Cs and 90Sr.
At each Ukrainian site, activity concentrations in soil at given years were decay corrected to April 1986 and initial deposition (kBq/m2) derived.
The initial deposition levels at each site were used to ‘scale-up’ the output from the model runs.
Activities in soil (total and ‘bioavailable’) and crops were derived.

## Slide 17: Model-model comparison – 137Cs in soil
The models provide quite divergent 137Cs activity concentration profiles.
At the end of the simulation period, level of 137Cs predicted using the ‘New’ fuel-particle soil model is 17 times greater than the prediction made using the FDMT model.
The ‘New’ fuel-particle soil model actually appears to predict very little loss of 137Cs from the top 20 cm of soil
  This is reasonably consistent with the general observed behavior of 137Cs in soil following the Chernobyl accident.
Chart: Time (days)
Notes: Figure xxx: 137Cs activity concentrations (Bq/kg) in soil with time (days) simulated using 2 models : ‘New’ fuel-particle soil model (turquois line) and FDMT (blue line); for Scenario 6 (South, high pH). Deposition = 1 kBq/m2 137Cs.

## Slide 18: Model-model comparison – 90Sr in soil
Both model simulations produce similar results for soil activity concentrations throughout the analysis period
The result might simply be coincidental
Overall losses from the soil system are similar
Notes: Figure: 90Sr activity concentrations (Bq/kg) in soil with time (days) simulated using 2 models : ‘New’ fuel-particle soil model (solid red line) and FDMT (dashed blue line); for Scenario 6 (South, high pH). Deposition = 1 kBq/m2 90Sr.

## Slide 19: Model-model comparison – 137Cs in grain
The model outputs are dissimilar.
Both FDMT and the Absalom models predict a continual decline in 137Cs in wheat,
The ‘New’ soil model does not attain maximum values before 4000 days.
At the end of the simulation period 137Cs in wheat, as predicted using the ‘New’ soil model, is about 15 x greater than that predicted using FDMT
Chart: Time (days)
Notes: Figure: 137Cs activity concentrations (Bq/kg) in wheat simulated using 3 models : ‘New’ fuel-particle soil model (solid red line), Absalom (blue dotted line) and FDMT (dashed green line); for Scenario 6 (South, high pH). Deposition = 1 kBq/m2 137Cs. The black, dash-dot line shows the Absalom model output using a default depth (over which 137Cs is assumed to be distributed) of 2.5 cm.

## Slide 20: Cs-137 activity concentration in grass
Identical temporal trajectory in the initial period (up to 50 days).
The profiles diverge substantially at later stages (post 100 days).
137Cs activity concentrations predicted by the new FP soil model fall relatively quickly before increasing gradually post 500 days,
The corresponding values from the FDMT model decrease continually falling substantially below the new model outputs when time passes several thousand days.
Notes: Figure: 137Cs activity concentrations (Bq/kg f.w.) in grass with time (days) simulated using 2 models : ‘New’ fuel-particle soil model (dashed blue line) and FDMT (solid orange line); for Scenario 6 (South, high pH). Deposition 137Cs = 1 kBq/m2 to soil, 50 kBq/m2 to vegetation.

## Slide 21: Cs-137 activity concentration in cow milk
The temporal trajectories for both models are identical in the initial 50-day period.
After approximately 4000 days, the 137Cs activity concentrations in milk predicted using the new FP model are substantially greater (i.e.by up to a factor of 10) than those predicted using FDMT.
Chart: Time (days)
Notes: Figure: 137Cs activity concentrations (Bq/L) in milk with time (days) simulated using 2 models : ‘New’ fuel-particle soil model (dashed blue line) and FDMT (solid orange line); for Scenario 6 (South, high pH). Deposition 137Cs = 1 kBq/m2 to soil, 50 kBq/m2 to vegetation.

## Slide 22
Regionalisation with adapting FDMT
Danyl Pérez Sánchez1, Ali Hosseini2, Justin Brown2, Nick Beresford3
CIEMAT, Spain,
DSA, Norway
UK CEH, UK

## Slide 23: Regionalisation
Regional modifications have been made to the FDMT model in ECOLEGO to better represent Norwegian and Spanish conditions as elaborated in CONFIDENCE D9.13.
This regionalisation can be split into two categories.
  The first of these relates to changes in underlying parameters using primarily datasets collated in the earlier projects COMET and HARMONE.
  The second modification pertains to the structure of component modules used in FDMT by replacement with test models.
Notes: The first of these relates to changes in underlying parameters using primarily datasets collated in the earlier projects COMET and HARMONE. These datasets are mainly related to (1) the growing season and harvest periods of crops and grass including seasonal development of Leaf Area Index and (2) animal feeding practice.

## Slide 24: Regionalisation in Norway, e.g. Lamb meat
The slaughter period for lambs is generally September–October and this provides most of the meat used for human consumption in the following year.
Modifications have been made to allow the user to select a date for lamb slaughter.
This date is then used to define the activity concentrations that are used as input to the calculation of human ingestion doses.

## Slide 25: Regionalisation in Norway (Reindeer)
Reindeer herding and husbandry is an important business in some parts of Norway,
Activity concentrations in reindeer meat would be substantially higher than those observed in lamb meat.
This reflects many factors that the most important is the diet of the animals throughout the year.
Whereas lambs are assumed to be fed on grass and hay, reindeer are assumed to feed primarily on lichen (winter) and grass and leafy shrubs (summer).
137Cs activity concentrations in reindeer and lamb meat with time following an (approximately) 1 kBq/m2 137Cs deposition event (see Brown et al., 2018).
Notes: parts of Norway, most notably in the Arctic, and reindeer meat and products can form a substantial part of the local population’s diet.
That simple exploratory exercise, evident that for the same level of deposition, activity concentWhereas lambs are assumed to be fed on grass during the summer and hay during the winter, reindeer are assumed to feed primarily on lichen in the winter returning to grass and leafy shrubs in the summer months.
rations in reindeer meat would be substantially higher than those observed in lamb meat.
Evident that for the same level of deposition, activity concentrations in reindeer meat would
The winter maxima and summer minima in reindeer meat shown this change in diet are quite conspicuous.
Whereas lambs are assumed to be fed on grass during the summer and hay during the winter, reindeer are assumed to feed primarily on lichen in the winter returning to grass and leafy shrubs in the summer months.

## Slide 26: Regionalisation in Spain
Changes have been made to account for :
Harvest period
Leaf Area Index
Crop yields
Transfer data
Notes: Harvest period: (Winter wheat, Spring wheat, Leafy vegetables, Grass (Intensive and Extensive)
LAI : Grass intensive and extensive
Crop yields: Winter wheat, Spring wheat, Leafy vegetables, Grass (Intensive and Extensive), potatos, oats, spring wheat

## Slide 27: Regionalization in Spain (Results)
Default: FDMT/ECOSYS-87 parameters alone
Spain+Default: Spanish regionalisation parameters with FDMT/ECOSYS-87 radioecological parameters
Spain+New Parameter: Spanish regionalisation parameters with updated radioecological parameters
Summarises maximum activity concentration predictions for winter wheat, leafy vegetables, cow milk and beef together with predictions five years after deposition using the three different parameter combinations.

## Slide 28: Concluding remarks
We now have a flexible tool which enables us to include process-based models. Demonstrated by adding:
  Absalom RCs model
  “hot particle” soil model
Including such models and comparing their outcomes with FDMT indicates that the current FDMT as used within post-accident decision support systems is likely fit-for purpose for ‘short-term’ predictions.
    Process-based models useful for longer-term predictions
We are easily able to conduct uncertainty and sensitivity analysis.
Potential importance of accounting for agricultural practices (e.g. slaughter date, growing season, harvest date) has been demonstrated.
We can now easily proceed towards regionalisation of the models.

## Slide 29: Thank you
For more information