## Slide 1: Block 4: Strategies involving stakeholders in the transition phase Scenario based facilitated discussion Introduction to the scenario
M. Montero1, C. Trueba1, R. Sala1, P. Nunes2, M. Reis3, I. Paiva3, B. García-Puerta1, T. Charnock4
1CIEMAT (Spain); 2APA (Portugal), 3IST(Portugal), 4PHE (United Kingdom)

## Slide 2: General objectives and method
In the transition phase much of the uncertainty raised from the deposition pattern has been addressed with monitoring etc. The situation requires:
  specific efforts to conclude the emergency response,
  and establishing specific response plans to begin the recovery / long term rehabilitation of the affected areas, supporting the return to normal social and economic activity, as far as possible
By the transition phase a lot of the uncertainty on the deposition pattern has been addressed with monitoring etc.
Introduction to the state of the scenario in the transition phase
Consequence management and preparedness for the recovery
  Strategy development in urban areas
  Actions in rural / agricultural areas
Focus on:
  Involvement of the stakeholders in the decision making process
  Decision criteria and actions taken in the transition phase
How to plan the establishment of optimal remediation strategies with stakeholder involvement in the decision-making process?

## Slide 3: Scenario in the transition phase
The release has ceased, the control over the source has been taken and urgent protective measures have been implemented to avoid the exposure to population, including evacuation, access restrictions and food restrictions.
The radioactive contamination has spread in the surroundings of the damaged NPP and transported and dispersed through near regions, affecting a both inhabited areas and relevant agricultural and farming systems.
The contamination level range and the affected areas have been identified.
It has to be decided how to proceed in such a situation. The actions to be taken will be focused on mitigating the consequences of the contamination and on preparing recovery plans on the urban and agricultural areas and the food-chain system affected.
For the purposes of this session, one member of one ensemble from WP1 is assumed to be the ‘real’ deposition pattern.

## Slide 4: Ground contamination (dry+wet) [Bq/m2] for 137Cs estimated through monitoring
Zoning

## Slide 5: Total potential effective dose [mSv] at ~ 7 days after start of release
≥ 100 mSv
Evacuation
Total Effective Dose (short term) [mSv]

## Slide 6: Total potential effective dose, except ingestion [mSv] at 1 year after start of release
Total Effective Dose (long term) [mSv]
≥ 100 mSv
PermanentRelocation
20 - 100 mSv
Restriction of use
Emergency exposure
situations
Existing exposure situations

## Slide 7: Land uses affected
CORINE LAND COVER 2012
Urban area
Grass area

## Slide 8: Summary of the situation
Zones with an emergency exposure situation:
  Zone with a permanent relocation (Tot Eff Dose 1y ≥ 100 mSv)
  Zone with some type of restriction of use (20 mSv ≥ Tot Eff Dose 1 y ≥ 100 mSv)
    Actions to reduce the effective dose to ≤ 20 mSv
Zone with an existing exposure situation (1 mSv ≥ Tot Eff Dose 1 y ≥ 20 mSv)
  Planning optimised strategies to recover the living conditions as soon as posible
For purposes of this demonstration the following áreas in the zone heavily contaminated have been selected:
  An urban area situated in the most populated zone and with a projected dose at 1 year after the deposition  20mSv
  The meadow areas at the North of this zone where we situate an agricultural system pasture-cow milk-milk.

## Slide 9: Block 4: Strategies involving stakeholders in the transition phase Scenario based facilitated discussion Urban Scenario

## Slide 10: Accident overview
Area where the mean predicted normal living dose in the first year >20mSv
The accident is large, and has impacted many areas of both Netherlands and Belgium. Areas have been evacuated and widespread temporary and permanent relocation is strongly indicated.
National resources are stretched and a high reference level dose for the post accident phase is indicated.

## Slide 11: Urban area of concern
Area where the mean predicted normal living dose in the first year >20mSv
The municipality of Cromstrijen is at the edge of the 20mSv.y-1 zone. It consists of the communities Klaaswaal and Numansdorp (townhall).

## Slide 12: Municipality Cromstrijen / Numansdorp
Province: Zuid Holland
Population: 8,716 (Numansdorp) + 4,047 (Klaaswaal)
Area of municipality: covers an area of 70,33 km² of which 15,96 km2 is water. Numansdorp occupy the 74% of the land with 39,88 km2 .
The built environment is generally brick houses; detached, semi-detached and modern terraces. Some light industry to the North.

## Slide 13: Consequences for Cromstrijen / Numansdorp
Contaminated surfaces in urban areas
  Roofs, walls
  Streets, pavements
  Areas of grass, garden(s)
  Playing grounds
  Sports fields
  Interiors
  …
Under the scenario the situation in Numansdorp, 7 days after the accident was supposed to be as follows:
  contamination  1 MBq/m2 137Cs
  doses ≈ 20 mSv/year

## Slide 14: Options for recovery (strategies)
Clean-up options
  Do nothing
  Lower waste: roof brushing, vacuum interiors, tree removal, plant removal, rotavating (grass/plant/bare-soil surfaces)
  Higher waste: roof replacement, vacuum interiors, plant removal, tree removal, top-soil removal grass/plant/bare-soil surfaces)
Relocation
  No relocation
  Relocation for 3 months after deposition
Combination of relocation and clean-up options 2 and 3

## Slide 15: Urban scenario. Projected residual doses in Numansdorp
See poster “Sources of uncertainty on ERMIN urban dose model” for more information on calculation

## Slide 16: Mean Individual dose 1st year due the recovery strategies
Chart: Mean annual dose, 1st year (mSv)
| None | Low waste | High waste | Relocation | LW + Rel | HW + Rel
Mean yearly dose (mSv/year) | 14 | 8 | 4.2 | 7.5 | 4.4 | 2.5
Yearly dose at 95% percentil is above  20 mSv
Compare to average exposure in NL: 2.6 mSv/a (2017)

## Slide 17: Number of cancer incidences during 50 years, attributed to the exposure (popul. and workers)
Chart: Number of fatal cancers added over 50 years after the accident
| None | Low waste | High waste | Relocation | LW + Rel | HW + Rel
Number of radiation induced fatal cancers during lifetime (population+workers) | 15.12 | 9.68 | 10.776 | 8.1021 | 5.7941 | 8.9421
Chart: Number of fatal cancers avoided over 50 years after the accident
| None | Low waste | High waste | Relocation | LW + Rel | HW + Rel
Number of avoided radiation induced fatal cancers during lifetime (population+workers) | 0 | 5.44 | 4.344 | 7.0179 | 9.3259 | 6.1779

## Slide 18: Cost
Costs of countermeasures taken into account during the discussions included following items:
  Relocation (housing)
  Compensation
  Production losses
  Direct cost for recovery strategy
  Radioactive waste transport and storage
  Health cost for fatal and nonfatal cancers

## Slide 19: Total costs
Chart: Total costs (M€)
| None | Low waste | High waste | Relocation | LW + Rel | HW + Rel
Cleanup | 0 | 21 | 83 | 0 | 21 | 83
Waste | 0 | 3.4967 | 68.95 | 0 | 3.4967 | 68.95
Health | 3.024 | 1.936 | 2.1552 | 1.6204 | 1.1588 | 1.7884
Relocation | 0 | 0 | 0 | 43.875 | 43.875 | 43.875
Low budget

## Slide 20: Urban scenario. Summary of quantifiable consequences of clean-up
* External dose from deposited radioactivity only
** Does not include cost of waste disposal or cost of relocation
*** Estimated from values used by WP4 Dutch panel (Twenhofel, C, 2018)
The estimations has been provided by Tom Charnock
1st year taken to be from 7days to 1year+7days
Strategy | No option | LW | HW | Relocation | LW+relocation | HW+relocation
*Mean individual dose 1st year mSv | 14 | 8.0 | 4.2 | 7.5 | 4.4 | 2.5
*95th % individual dose 1st year mSv | 22 | 11 | 7.9 | 11 | 7.1 | 4.4
Mean duration >5mSv/yr (days) | 1000 (» 3 y) | 300 (»1y) | 26 | 1000 | 300 | 26
95th % duration >5mSv/yr (days) | 1700 (» 5 y) | 750 (» 2y) | 170 | 1700 | 750 | 170
Mean coll dose for population (person Sv) | 378,00 | 216,00 | 113,40 | 202,50 | 118,80 | 67,50
*Mean coll worker dose (person Sv) | 0,00 | 26,00 | 156,00 | 0,05 | 26,05 | 156,05
Induced fatal cancers during lifetime (population+workers) | 15 | 10 | 11 | 8 | 6 | 9
Mass of waste (1000Kg) | 0 | 7,1 | 140 | 0 | 7,1 | 140
Cost for cleanup strategy (implementation) in M€ | 0,00 | 21,00 | 83,00 | 0,00 | 21,00 | 83,00
***Cost for waste transport and storage (50+ years) in M€ | 0,00 | 3,50 | 68,95 | 0,00 | 3,50 | 68,95
***Cost for relocation and compensations in M€ | 0 | 0 | 0 | 44 | 44 | 44
***Cost for cancer treatments (exclusive loss of life/productivity) in M€ | 3 | 2 | 2 | 2 | 1 | 2

## Slide 21: Urban scenario. Unquantifiable consequences
Other factors more difficult to quantify should be also taken into account to assess the success of the strategies
The biggest uncertainty is probably how much the consequences of the accident in other regions will impact on this town, ie.
  disruption to supply chains
  employment availability
  customer demand
Other suggestions:
  Psychosocial consequences
  Prevent anxiety
  Acceptance of the protective actions and recovery strategy
  Perception of the risk for the consumer
  Protection of export
  Independence population
  Trust on the authorities

## Slide 22: Block 4: Strategies involving stakeholders in the transition phase Scenario based facilitated discussion Agricultural Scenario

## Slide 23: Overview of accident. Affected areas.
Restriction of local food consumption and grazing as precautory action
Food screening
 MPLs
Contaminated zones

## Slide 24: Agricultural áreas of concern.
Area where the activity concentration in some agricultural product > maximum permissible level (MPL) for commercialisation
Relevant pathway
  Pasture-cow-milk-cheese

## Slide 25: Consequences
Contamination and transfer to:
  Soils
  Crops
  Food-chain (products)
Under the scenario the situation in Zuid-Holland, 7 days after the accident was supposed to be as follows:
  contamination  1 -10 MBq/m2 137Cs
  Activity concentration
    in grass ≥ 5000 Bq/Kg
    in milk ≥ 1000 Bq/Kg

## Slide 26: Temporal evolution of the activity concentration of 137Cs in agricultural products. Zoning according the MPLs [Bq Kg-1]
1 day
1 year
5 years
20 years
Grass I
≥ 5000
1 day
1 year
5 years
20 years
Cow milk
≥ 1000
1 day
1 year
5 years
20 years
Winter Wheat
≥ 1250

## Slide 27: Recovery alternatives
Do nothing, implementing a monitoring strategy
On the Soil, to reduce the transfer of contamination to the food-chain:
  Chemical treatments: Application of Potassium fertiliser
  Mechanical treatments:
    Deep ploughing
    Top soil removal
On the cattle, to reduce the activity concentration on the animal products:
  Supply clean fodder
  Administration of AFCF
On the foodstuffs:
  Proccesing of milk for human consumption

## Slide 28: Recovery actions in soil
Grass – K-fertilisation effect
K Ammendment
Amount: 100 kg/ha.y = 0,1 meq/100 g
0,46
0,72
0,92
Clay: 18 -35 %
Exch K : 0,47 - 0,55 meq/100g
Typical soils:
Effectiveness (TFf/TF0) = 0,72
April

## Slide 29: Temporal evolution of the activity concentration through pathway grass-cowmilk - milk
Chart: Activity concentration of Cs-137 in pathway grass-cowmilk -milk

## Slide 30: Uncertainties raised when planning the implementation of the recovery strategy
Issues in the agricultural environments
  Zoning? Constrains? Reference levels?
  Identification of product systems / soils / pathways /products / population groups more vulnerable
  Prognostic versus monitoring results? In which cases should these results be used? How to obtain a balanced use?
  Selection and establishment of strategies. How to apply the optimisation principle?
  Effects influencing the decision and future evolution of scenarios: Social, Technological, Economic, Environmental, Political and Ethical values. Criteria to measure them.
How to translate these issues into goals and objectives suitable for the restoration of agricultural environments?
The cessation of production or restriction in consumption are actions in the emergency phase, but difficult to keep over time; economic compensation?
Are there enough resources (material, human, economic, technical) to implement the different options?
What will be the effects on the food distribution chain? Possible socio-economic impact.

## Slide 31: Facilitated discussion questions
Which are the main concerns when facing the recovery strategy?
What are the objectives to pursue in the recovery strategy?
What are the main factors and key criteria for the strategy selection?
What are the main uncertainties affecting the decision about the recovery strategy?
Choose the strategy you think it is best according to the previous discussions

## Slide 32: Support Material

## Slide 33: Urban countermeasures (selection from EURANOS Handbook)

## Slide 34: Agricultural countermeasures (selection from EURANOS Handbook)

## Slide 35: Agricultural countermeasures (selection from EURANOS Handbook)

## Slide 36: Factors influencing selection of management options (EURANOS Food Hanbook)

## Slide 37: Scenario based facilitated discussion Block 4: Strategies involving stakeholders in the transition phase Introduction to the scenario
milagros.montero@ciemat.es