## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
Ensemble simulations on the Fukushima case study and comparisons to observations
Irène Korsakissok1, Raphaël Périllat2,, Susan Leadbetter3
With contribution of WP1 participants to the Fukushima study
2IRSN, PSE, Fontenay-aux-Roses, France, 2PHIMECA ENGINEERING, Clermont Ferrand, France, 3Met Office, Exeter, UK
Irene.korsakissok@irsn.fr
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Indicators to assess the quality of an ensemble by comparison to observations
Conclusion
Wp1
Performance of the ensembles’ medians
Korsakissok, I., R. Périllat, S. Andronopoulos, P. Astrup, P. Bedwell, E. Berge, A. Quérel, H. Klein, S. Leadbetter, O. Saunier, A. Sogachev, J. Tomas and M. Ulimoen (2019). D 9.5.3 Ensemble calculation for a past accident scenario: the Fukushima case study. D9.5 Guidelines for the use of ensemble calculations in an operational context, indicators to assess the quality of uncertainty modeling and ensemble calculations, and tools for ensemble calculation for use in emergency response, European Joint Program for the Integration of Radiation Protection Research CONCERT - CONFIDENCE project.
Design of a meteorological ensemble
The ECMWF Integrated Forecast System was used to create a 72 hour ensemble forecast starting 00:00UTC 14 March 2011 with the following specification:
Ensemble members: 1 control and 50 perturbed members
Spatial coverage: 32°N to 43°N and 134°E to 148°E
Spatial resolution: 0.2° (~22km)
Temporal resolution: 1 hour
Vertical resolution: 36 levels
Ensemble of source terms
9 source terms (ST) from the literature are used in this study
Differences in kinetics, global quantity, isotopic composition
 | Source term | Total 137Cs (PBq) | March 14-16th 137Cs (PBq) | Observations used
1 | Stohl et al. (2011) | 35.7 | 21.4 | Concentrations in the air over the entire Northern Hemisphere. Facility events.
2 | Winiarek et al. (2012) | 10-19 | 3.1 | Concentrations in the air over Japan and North America.
3 | Terada et al. (2012) | 8.7 | 4.9 | Concentrations in the air over Japan. Dose rates close to FDNPP. Facility events.
4 | Mathieu et al. (2012) | 20.6 | 13.2 | Concentrations in the air over Japan. Dose rates close to FDNPP. Facility events.
5 | Saunier et al. (2013) | 15.5 | 6.5 | Dose rates in Japan.
6 | Kobayashi et al. (2013) | 13 | 10.6 | Depositions over the sea. Concentrations in air over Japan. Dose rates close to the facility. Facility events.
7 | Katata et al. (2015) | 14.1 | 5.3 | Concentrations in the air over Japan. Dose rates close to FDNPP. Depositions over the sea.
8 | Yumimoto et al. (2016) | 8.12 | 3.2 | Total deposition over Japan.
9 | Saunier et al. (2016) | 8.1 | 3.1 | Concentrations in the air over Japan.
Introduction
The Fukushima disaster occurred in March 2011, triggered by an earthquake followed by a tsunami. Radioactive materials were released in the atmosphere by the damaged reactors, mostly during the 3 weeks following the earthquake. It resulted in significant contamination of the air and ground in Japan. Two release periods were observed to be responsible for the highest contamination on Honshu island, the first one on March 14-16th and the second one on March 20-22nd. The first 3-day episode was retained for study in CONFIDENCE WP1 (Korsakissok et al, 2019). Even eight years after the accident, uncertainties remain high. Meteorological fields are difficult to reproduce, due to complex orography, stable situations, low wind speeds and precipitation episodes. Source terms are also subject to high uncertainties and their assessment still relies on the combination of facility events, radiological observations, meteorological and dispersion modelling. In the CONFIDENCE project, meteorological and source term uncertainties were propagated through atmospheric dispersion models by six participants and compared to radiological observations. This poster presents some statistical indicators to compare the ensembles’ outputs with observations in order to assess their quality.
The Rank histogram is a method to estimate if an ensemble is representative of the observed uncertainty. It indicates the ability of the ensemble to encompass the observations.
The rank of an observation is determined by counting how many members of the ensemble are below this observation. The rank histogram shows the number of observations of each rank counted on all stations and time steps. Theoretically, a “perfect” rank histogram would be flat, indicating no bias in the model results. An under-dispersive ensemble is U-shaped, indicating there are uncertainties not (well) taken into account; an over-dispersive ensemble would be ∩-shaped.
The Brier score is defined as follows:
Where is the probability of exceeding a given threshold according to the ensemble (between 0 and 1) and is the outcome, given by the observation (1 if the threshold is exceeded, 0 otherwise). Therefore, the closer to zero the score is, the better the ensemble is at forecasting the probability of threshold exceedance. The Brier score can then be plotted against different possible thresholds.
From the results of the ensemble run, the ensemble median can be used, as a “representative” simulation resulting from taking into account all uncertainties. Deterministic model-to-observations statistical scores can then be computed.
If are the scalar observations and are the corresponding values of the representative simulation (for in with the number of observations), then we can define the Root Mean Square Error and the Pearson Correlation Coefficient by:
Air concentration scores for 137Cs | DTU | EEAE | IRSN | NMI | MO | RIVM
RMSE (Bq/m3) (× 102) | 5.57 | 1.83 | 2.07 | 1.90 | 2.54 | 1.93
PCC | 0.23 | 0.36 | 0.22 | 0.45 | 0.23 | 0.26
FMT (%) | 41.7 | 46.5 | 63.8 | 26.3 | 32.6 | 28.9
FAC2 (%) | 10.3 | 11.8 | 18.7 | 4.9 | 8.5 | 6.6
FAC5 (%) | 24.5 | 26.4 | 41.7 | 13.2 | 18.8 | 16.2
Dose rate scores | DTU | EEAE | IRSN | NMI | MO/PHE | RIVM
RMSE (nSv/h) (× 103) | 4.95 | 4.85 | 4.92 | 6.70 | 4.81 | 9.23
PCC | 0.33 | 0.34 | 0.37 | 0.15 | 0.38 | 0.04
FMT (%) | 81.3 | 79.3 | 97.8 | 93.5 | 97.2 | 89.7
FAC2 (%) | 37.7 | 38.6 | 41.4 | 41.4 | 43.4 | 20.1
FAC5 (%) | 74.1 | 73.3 | 77.5 | 83.8 | 77.1 | 47.7
The “best” score is obtained by different participants depending on the variable and score.
4 out of 6 participants have the “best” score at least once.
The performance of some ensembles’ medians is comparable to what can be achieved by ‘best estimates’.
Deterministic scores of ensembles’ medians for the 6 participants to the Fukushima study, for air concentrations and gamma dose rates.
IRSN
Met Office
EEAE
DTU
RIVM
NMI
Rank diagrams of the ensembles for the 6 participants to the Fukushima study. Left: air concentrations of 137Cs; right: gamma dose rates.
IRSN
Met Office
EEAE
DTU
RIVM
NMI
Brier scores of the ensembles for the 6 participants to the Fukushima study, as a function of the threshold. Upper: air concentrations of 137Cs; lower: gamma dose rates.
Statistical indicators were used to compare the ensembles’ outputs with observations (air concentrations of 137Cs and gamma dose rates) in order to assess their quality. First, deterministic scores for the ensembles’ medians showed that, among the 6 different ensembles, four of them had the best score at least once for a given indicator and variable. Then, probabilistic scores were used to evaluate the ability of the ensembles to represent the overall uncertainties. Two complementary indicators were shown: the rank diagram indicates the ability of an ensemble to encompass the observations, while the Brier score represents its capability to forecast the exceedance of a given threshold. Overall, all ensembles show an acceptable performance according to these indicators. This could be further completed by extending the study to the 3 weeks of release and comparing the results to deposition measurements.
Rank diagrams for air concentrations show a bias toward underestimation
Rank diagrams for dose rate are good but not totally flat for all participants
Air concentrations: Brier scores for all participants are very close for thresholds >1 Bq/m3
Dose rates: The “best” model differs when considering high and low thresholds
The Figure of Merit in Time (FMT) is a score based on a threshold. If and are the ensembles of time steps where respectively the measurement and the prediction are above the given threshold, and if is the cardinality of an ensemble (i.e. the number of elements in the ensemble), then:
The FACX scores are the percentage of which are within a factor X of the observations, i.e. between and .
A “perfect” model would have RMSE=0, PCC=1, FMT=100% and FACX=100%.