## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
Design of an ensemble of source terms representative of uncertainties in case of a severe nuclear accident
Karine Chevalier-Jabet1, Irène Korsakissok2, Anne Mathieu2, Raphaël Périllat3
1IRSN, PSN, Cadarache, France
2IRSN, PSE, Fontenay-aux-Roses, France
3PHIMECA ENGINEERING, Clermont Ferrand, France
karine.chevalier-jabet@irsn.fr
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Ensemble of source terms used in the CONFIDENCE project
Conclusion
An ensemble of source terms was extracted from the database built with the ASTEC severe accident code. The chosen scenario was a LOCA accident with a break of 3 inches on the hot leg. For this scenario, uncertainties taken into account included on the break size (+/- 1 inch), system availability, leak rate and distribution, mass of corium slump, iodine behaviour and MCCI-related variables. This resulted in a variability of up to 2 decades on the released quantities for some radionuclides. Among the 150 source terms, significant differences are shown in the release kinetics, in particular in the timing of the second release (corresponding to the opening of the venting containment system), which can occur between 10 to 60 hours after the opening of the break. Therefore, no simple multiplicative factor may be used to account for these uncertainties.
A subset of this ensemble of source terms was further propagated through ADMs, using the REM meteorological datasets – as shown in CONFIDENCE presentations.
Wp1
Release of Iodine and Xenon is much higher: large 2nd release where aerosols are filtered
There is a high variability in the release rates (up to 2 decades)
The kinetics are complex (iodine chemistry…): not a simple multiplicative factor
Choice for the REM scenario: 3 inches, hot leg – necessity to reduce to 10 source terms
Extract from the FASTNET database: 4 ensembles of ~150-200 source terms
3 inches variability +/- 1 inch, hot leg
3-days release
No (or small) uncertainty on beginning release
Second major release = opening of the venting containment system
Maximum, minimum, percentiles of released quantities for several radionuclides on the ensemble of source terms (3 inches, hot leg)).
3 inches break | 132Te | 137Cs | 133Xe | 131I | 132I | 136Cs | 134Cs | 137mBa
Maximum |  |  |  |  |  |  |  | 
75th percentile |  |  |  |  |  |  |  | 
50th percentile |  |  |  |  |  |  |  | 
25th percentile |  |  |  |  |  |  |  | 
Minimum |  |  |  |  |  |  |  | 
3 inches break | 132Te | 137Cs | 133Xe | 131I | 132I | 136Cs | 134Cs | 137mBa
Maximum |  |  |  |  |  |  |  | 
75th percentile |  |  |  |  |  |  |  | 
50th percentile |  |  |  |  |  |  |  | 
25th percentile |  |  |  |  |  |  |  | 
Minimum |  |  |  |  |  |  |  | 
Modelling reactor physics during a severe accident
In addition, safety systems may be used, if available:
Safety injection (SI)
Containment spray system (CSS)
Containment venting system
Venting and filtration system
Ultimate Safety systems: passive sumps alkalinisation, additional cooling systems
In addition, complex iodine-related phenomenology take place in the containment.
Important phenomena include:
Core degradation
Containment pressure build up
Ex-vessel radioactive release
Vessel rupture
Molten corium-concrete interaction (MCCI)
Dewatering of the core to such an extent that fuel degradation can occur and result in the release of radioactive species. This is called a LOCA accident (Loss of Cooling Accident).
Introduction
In case of a nuclear accident, uncertainties on the source term are the prime source of uncertainties in atmospheric dispersion modelling (ADM), along with meteorology.
The input variables related to source terms are the timing of major releases, released quantities, and isotopic composition. In addition, particle size and variables related to plume rise (temperature and exit velocity) may also be of value, although more difficult to assess, and of secondary importance for the ADM calculations. The uncertainties on these variables stem from lack of information (on availability of systems, operators actions…), partial understanding of physical phenomena that take place in the reactor during an accident (epistemic uncertainties), human errors, modelling tools and methods.
Integral severe accident reference codes offer the opportunity to study in detail severe accident scenarios, including the evaluation of source terms. The computer time needed to evaluate the outcome of a given scenario makes the use of these codes impossible in the context of emergency situation. In order to benefit from the knowledge of Integral severe accident reference codes, one can however rely on pre-calculated scenarios. In the framework of the FASTNET project the use of Bayesian Networks, in addition of other tools, was investigated (Chevalier Jabet et al, 2019). An extract of this database was used as input to the CONFIDENCE project to perform ensemble simulations for the so-called REM-long release scenario. The primary goal was to to gain knowledge on the uncertainties related to source terms for a chosen accident scenario. The aim is to have an ensemble of source terms, including the release kinetics for all relevant isotopes (i.e. released quantity as a function of time), whose spread is representative of the uncertainties. They can then be further propagated through atmospheric dispersion models to infer their impact on relevant endpoints such as doses and deposition.
Use of the severe accident code ASTEC to compute a source term database that takes into account uncertainties
FASTNET: European project dedicated to harmonize approaches to manage nuclear emergencies among European entities, and share knowledge on severe accidents phenomenology. Within WP2, IRSN constructed a database using machine learning techniques on a set of pre-calculated scenarios by the ASTEC (Chatelard et al., 2014) severe accident code.
Uncertain variables related to the scenario:
Break size 3 or 12 inches
Break position: can be on cold leg or hot leg
Systems: no safety injection (SI) available; CSS can be working or not at the initiator time;
Release rate of fission products (FP) the containment building,
release routes.
At vessel rupture, mass of the corium slump
Uncertainties taken into account:
Variability on break size +/- 1 inch
Release rate of FP from containment building [1; 10]
distribution of the leak rate from main containment to the auxiliary buildings [1; 2] times the best-estimate value.
if vessel rupture, mass of corium slump in the cavity may range from [1/2; 1] times the amount of corium left in the lower head at vessel rupture
FP release from fuel: from a few % to 200% (depends on FP)
Iodine behavior
MCCI-related uncertainties are around [~10%]
The input deck models a French PWR 900 MW. The initiating event is the opening of a break on the primary circuit. The calculation stops after 72 hours.
(a) 133Xe
(c) 137Cs
(d)
(b) 131I
References: Chatelard, P., N. Reinke, S. Arndt, S. Belon, L. Cantrel, L. Carenini, K. Chevalier-Jabet, F. Cousin, J. Eckel, F. Jacq, C. Marchetto, C. Mun and L. Piar (2014). "ASTEC V2 severe accident integral code main features, current V2.0 modelling status, perspectives." Nuclear Engineering and Design 272: 119-135
Chevalier-Jabet, K. (2019). Design and use of Bayesian networks for the diagnosis/prognosis of severe nuclear accidents, EU program for research and innovation H2020 - FAST Nuclear Emergency Tools (FASTNET) project. Report FASTNET-DATA-D2.3.
(a), (b), (c): Evolution of the emitted quantity of different radionuclides for the break of 3 inches occurring on hot leg. The x-axis gives the hours after the opening of the break The blue lines represent the release rates for the different source terms of the ensemble. (d): Histogram of the timing for opening the containment for all source terms.
Opening of the venting containment system
Sand bed: aerosols are filtered