## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
Efficiency savings in model setup for an ensemble approach used to describe atmospheric dispersion model uncertainty Csilla Rudas, Péter Szántó, Tamás Pázmándi, Péter Zagyvai
Centre for Energy Research, Budapest, Hungary rudas.csilla@energia.mta.hu
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Introduction
Calculation
Conclusion
References
Results and discussion
In emergency preparedness and response, the decisions made to protect the public in case of a severe nuclear accident have to be reliable, profound and made quickly. To achieve this a) the uncertainty of the results has to be shown and b) the runtime of simulation has to be feasible (reasonably short). When using meteorological ensemble datasets in atmospheric dispersion modelling, the impact of uncertainty is directly reflected in the result, but the runtime of the simulation is significantly increased. In this poster we examine different methods of reducing model run time for a single ensemble member and assess the change in the uncertainty indicators [1]. The simulations were performed with SINAC (Simulator Software for Interactive Consequences of Nuclear Accidents) decision support system [2] developed in the Centre for Energy Research. The meteorological ensemble data used for the simulation was produced by HARMONIE-AROME model with a horizontal resolution of about 2,5 km on a 300 km x 300 km domain [3].
The dispersion calculation in SINAC is performed with a Gaussian Puff Model as follows:
Initialization: initiating run, reading the meteorological data, and reserving memory space for the results
Dispersion: propagation until the puffs reach the maximum time or maximum distance set as an input parameter
Results: calculating activity concentrations and doses for all receptor points and writing the result into the output files
CHEAPER DISPERSION MODELLING SCHEME
First method of reducing run time is changing the number of puffs released. The total released activity is the same divided uniformly among the released puffs. Changing the number of released puffs released from the original 16 to 4 and then to 64 affects the run time of the simulation shown in the Table 2.
[1] Bedwell, P. et al., 2019: Guidelines for the use of ensembles in the description of uncertainty in atmospheric dispersion modelling: operational applications in the context of an emergency response. CONFIDENCE Report D72
[2] Szántó, P. et al., 2012: SINAC – Simulator Software for Interactive Modelling of Environmental Consequences of Nuclear Accidents (2nd Generation), 13th International Congress of IRPA, 13-18 May 2012, Glasgow, Scotland.
[3] De Vries, H. et al., 2019: Published sets of probability maps of threshold exceedance for scenarios. CONFIDENCE Report D9.4
Model setup efficiency savings have been identified such that model runs in an ensemble approach (for the scenario outlined/referenced) can be performed within a practical timeframe for assessing exposure situations, without detriment to the description of atmospheric dispersion model uncertainty.
WP1
Number of puffs [#] | 4, 16, 64
Time resolution of puff propagation [min] | 4, 8, 16
Model domain [km x km] | 254x254, 510x510, 767x767
Results grid [number of points] | 100x100, 200x200, 300x300
Maximum time of simulation [hour] | 36
Maximum distance of simulation [km] | 400, 500, 600
Time resolution of output [hour] | 1, 2, 4
Table 1: The input parameters of the simulations, reference values indicated with bold.
The different temporal resolutions did not affect the mean maximum distance and surface values of threshold exceedance. The overall appearance of the Cs-137 time series plots (Figure 3.) is very similar for the different temporal resolutions of the shown output. Because the deposition is an integrated variable it is less sensitive to the temporal resolution than for example considering the time series of air concentration and gamma dose rates.
Number of puffs | 4 | 16 | 64
Initialization [s] | 44 | 45 | 41
Dispersion [s] | 27 | 26 | 27
Results [s] | 213 | 386 | 1004
Total run time for 10 ensembles [s] | 2840 | 4570 | 10720
Table 2: Mean run time (per ensemble member) for each step of the calculation process and the total run time over all ensemble members and all steps of the calculation process, calculated assuming variable numbers of released puffs.
Figure 1: Maximum distance (in km from the source) of threshold exceedance for the mean of the ensemble results, for several model endpoints and for three simulation cases. Bars indicate standard deviation of the results.
The main contributor (75-85%) to the total run time was the time for calculating and writing the results. Reducing the number of released puffs to one-quarter decreased the run time to only 48 minutes, and multiplying it 4 times increased it to almost 3 hours. Results shown in Figure 1. indicate that considering 64 puffs instead of 16 is not justified, because considering these quantities the results for the two simulations are remarkably similar. However, with the release of 16 puffs rather than 4 puffs, the standard deviation and thus the uncertainty of the Cs-137 deposition results was significantly reduced.
MODIFIED MODEL DOMAIN
Changing the spatial domain of the calculation (Figure 2) and the grid of the output significantly reduced the run time of the simulation shown in Table 3.
Spatial domain [number of grid points] | 300x300 | 200x200 | 100x100
Initialization [s] | 45 | 9 | 1
Dispersion [s] | 26 | 27 | 27
Results [s] | 386 | 133 | 28
Total run time for 10 ensembles [s] | 4570 | 1690 | 560
Table 3: Mean run time and total run time for 10 ensemble members calculated with different spatial domains and numbers of output receptor points.
Chart: Spatial Grid
| 3.718
Release point | 51.43
300x300 | 49 | 55.88 | 55.88 | 49 | 49
200x200 | 49 | 53.58 | 53.58 | 49 | 49
100x100 | 50.26 | 52.54 | 52.54 | 50.26 | 50.26
Figure 2. The spatial domain of the simulation and the release location.
By reducing the domain to 4/9 and 1/9 of its original size, the runtime was reduced by approximately 37% and 13%, respectively. The major reduction was achieved in the calculation of results, because there were much fewer receptor points in the smaller domains. The ensemble mean maximum distances and surface of threshold exceedance did not change with the reduction of the considered spatial area because these areas were within the borders of the smaller domains for all the ensembles.
ALTERNATIVE TEMPORAL RESOLUTION OF THE OUTPUTS
Changing the temporal resolution of the time integrated activity concentration in air and deposition concentration output from 1 hour to 2 and 4 hours resulted in only a 22-26% reduction in total run time shown in Table 4.
Time resolution of output [hour] | 1 | 2 | 4
Initialization [s] | 45 | 42 | 45
Dispersion [s] | 26 | 26 | 26
Results [s] | 386 | 289 | 269
Total run time for 10 ensembles [s] | 4570 | 3570 | 3400
Table 4: Mean run time and total run time for 10 ensemble members calculated whilst varying the temporal output resolution.
a) | b)
Figure 3: Time series of the Cs-137 deposition concentration averaged over the domain for 10 ensembles calculated with output time resolution of (a) 1 hour, (b) 4 hours.
Chart: 
| Cs-137 Deposition 10 kBq/m2 | Effective Dose 1 mSv | Inhalation Thyroid Dose 10 mSv
4 puffs | 164.3765 | 36.7275 | 82.1065
16 puffs | 132.1405 | 33.8356 | 78.9822
64 puffs | 130.7397 | 33.1761 | 77.8328