## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
Analysis of the REM2 Case Study using Numerical and Graphical Techniques
Susan Leadbetter1, Peter Bedwell2, Gertie Geertsema3, Irène Korsakissok4, Jasper Tomas5, Hans de Vries3, Joseph Wellings2
1Met Office, Exeter, UK, 2PHE, UK, 3KNMI, the Netherlands, 4IRSN, Fontenay-aux-Roses, France, 5RIVM, the Netherlands
susan.leadbetter@metoffice.gov.uk
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
The REM2 Case Study
Conclusions
Combining Meteorological and Source Term Uncertainty
The second REM case study (REM2) was chosen to coincide with the passage of a warm front. The timing of the front passage varied between ensemble members. The wind direction was initially from the south to the north and between 18:00 and 20:00 UTC altered to be from the north-west to the south-east. Immediately after the wind direction change the wind speed increased from around 5m/s to around 10m/s. Precipitation was around 2mm/hr as the front approached and increased to 4mm/hr as the front passed before decreasing to 0mm/hr. Previous work has shown that 4mm/hr can reduce the air concentration in a plume by 50% in less than 1 hour (Leadbetter, 2019).
The REM2 case study highlights the impact of heavy precipitation on air concentration and deposit predictions. The case also shows how small uncertainties in wind direction close to the source can cause significant differences in the location of dose threshold exceedances.
The REM2 case study demonstrates how the overall uncertainty can be increased by timing uncertainty in the source start time combining with rapidly changing meteorology.
Wp1
Cs137 37kBq/m2 deposition. contour
Wind Speed
Wind Direction
Precipitation
Meteorological Ensembles
Cs137 37kBq/m2 deposition contour. Different colours represent different meteorological ensemble members. Subplots are different release start times.
Thyroid Inhalation 10mSv contour
Thyroid Inhalation 10mSv contour. Different colours represent different meteorological ensemble members. Subplots are different release start times
Meteorological information for dispersion models is typically obtained from Numerical Weather Prediction (NWP) models as 3D or 4D fields of variables such as wind speed and direction, boundary layer height and precipitation. Most dispersion models used in emergency response take information from a single NWP. However, the atmosphere is a chaotic system meaning that small deviations from the initial conditions can grow quickly. Meteorological modellers overcome this by running meteorological models several times with slightly different initial conditions and slightly different model parameterisations (see Leadbetter et al., 2018 for more details). This is an example of an “ensemble” models. Ensemble models were first used in the 1990’s.
Ensemble meteorological data for the REM case study was provided by KNMI using the Hamonie-AROME model (Geertsema, 2019). The ensemble was constructed from two different versions of the model with different turbulent schemes, and combined successive deterministic forecasts to create a 10-member hybrid lagged ensemble (more detail in presentation).
Wind direction (degrees), wind speed (m/s) and precipitation rate (mm/hr) at the release site between 15:00 UTC 12/01/2017 and 03:00 UTC 13/01/2017.
Impact of Meteorological Uncertainty
Default Source Term
Release time: 21:00 12/01/17 Release height: 50m
Release duration: 4 hours Release rate: constant
Radionuclides: I-131, I-132, Te-132, Cs-134, Cs-136
Cs-137, Ba-137m, Xe133
A default source term was used by all participants
The default start time is after the passage of the front over the release location so radioactive material is transported to the south-east.
The wind direction ensemble members 3, 4, 8 and 9 results in a plume that is located slightly further north. The wind speed is slightly higher in these ensemble members resulting in the 10mSv thyroid threshold being exceeded over greater distances.
The regions where a 10mSv thyroid inhalation dose threshold was exceeded differs significantly between ensemble members.
The front passes before the start of the release but the plume encounters the front in the first few hours.
Light precipitation covers most of the domain close to the release location.
The maximum frontal precipitation rate is lower in ensemble members 3, 4, 8 and 9 and in these ensemble members the front travels further to the east.
Thus, there is a significant difference in the predicted location of the highest deposits (Cs137>37kBq/m2)
The delayed timing of the precipitation results in the deposit threshold being exceeded at greater distances in members 3, 4, 8 and 9.
The source term was perturbed by assuming that the timing of the release was uncertain. Here we show three different release times, +/- 6 hours from the default release time and the default release time: 15:00 12/01/2017, 21:00 12/01/2017 and 03:00 13/01/2017.
The release duration, height, rate and radionuclide composition were kept the same in all runs
NAME was run with each source term combined with each of the 10 meteorological ensemble members resulting in a combined ensemble of 30 members.
Material released at 15:00 travels in a northerly direction. Material released at 21:00 and 03:00 travels to the south-east and east respectively.
The region where the thyroid inhalation dose exceeds 10mSv is much more elongated for the 21:00 and 03:00 releases. This is partly because wind speeds are higher after the front passes and partly because the plume of material released at 15:00 is washed out of the atmosphere by the heavy frontal precipitation.
The region where the Cs137kBq/m2 deposition threshold is exceed is very small for the 15:00 release because material is washed out very close to the release point.
Different colours represent different met ensemble members
Precipitation rate in each of the 10 met ensemble members at 23:00 UTC 12/01/2017, 2 hours after the start of the release. Maximum precipitation rates are around 4mm/hr.
15Z 12/01
21Z 12/01
03Z 13/01
NAME (dispersion model)
NAME (Numerical Atmospheric-dispersion Modelling Environment) is a Lagrangian particle model developed and maintained by the UK Met Office (Jones et al., 2007). NAME models the transport and deposition of gases and particles at a range of scales from a few kilometres to a few thousand kilometres. Particles are advected by the ambient three-dimensional wind field provided by a meteorological model with turbulent dispersion processes being simulated using random-walk methods.
Material is removed from the atmosphere by dry and wet deposition processes. The removal of material from the atmosphere by wet deposition is based on the air concentration and a scavenging coefficient that depends on the rainfall rate and 2 coefficients which vary for different types of precipitation (rain or snow) and for different wet deposition processes (in-cloud and below-cloud). NAME also simulates the decay of radioactive particles.
 | Rain
Below-cloud (washout) | A = 8.4 x 10-5 B = 0.79
In-cloud (rainout) | A = 3.36 x 10-4 B = 0.79
Scavenging parameters used in NAME
The scavenging coefficient is given by: Λ=ArB
Where r is the rainfall intensity in mm/hr
References
Geertsema, 2019. High Resolution Meteorological Ensemble Data for CONFIDENCE Research on Uncertainties in Atmospheric Dispersion in the (Pre-) Release Phase of a Nuclear Accident, Harmo 2019, Bruges, Belgium.
Jones, A.R., et al., 2007. The U.K. Met Office’s next-generation atmospheric dispersion model, NAME III, in Air Poll. Model. and App. XVII, Springer, pp. 580-589.
Leadbetter, S., et al. 2018. D1.1.1 in D9.1 Guidelines ranking uncertainties for atmospheric dispersion, CONCERT - CONFIDENCE project.
Leadbetter, S.J., Use of Radar Rainfall to Model Deposition of Radionuclides, Atmos. Env., 211, 181-193, 2019
15Z 12/01
21Z 12/01
03Z 13/01