## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
A Mobile App for Thyroid Dose Assessments in a Nuclear Emergency (WP2)
Gennadii Ratia , Volodymyr Berkovskyy, and Iurii Bonchuk
Ukrainian Radiation Protection Institute, Kyiv, Ukraine
ratia@rpi.kiev.ua
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Introduction
Objectives
Materials and methods
Discussion
Conclusion
Results
In a nuclear emergency, dealing with uncertain information is a fundamental problem for decision making. The reduction of uncertainty, as well as minimisation of the time for decision making, is crucial to improving the protection of the affected population in case of a severe nuclear accident. The CONFIDENCE task within CONCERT (Task 9.1) aims to improve decision making for the protection of the people affected by a nuclear emergency through the reduction of uncertainties and elaboration of approaches to deal with uncertainty information. Subtask 2 (ST 9.1.2) is dedicated to the development of approaches and tools integrating external and internal dosimetric monitoring data to obtain a comprehensive picture of the radiological situation and link it with dose and risk assessment tools to support the decision making and medical follow-up.
This work is focused on the development of a prototype of the smartphone-based data processing unit (DPU) and the underlying methodology for processing of the thyroid monitoring data, thyroid dose assessment and mitigation of uncertainties of estimations. The features of the tool involve all available information about the exposed individual, history and conditions of exposure, as well as the radionuclide composition of the source term.
An assessment of the thyroid absorbed dose or committed effective dose from bioassay measurements can be performed with ‘dose per content’ functions that directly relate the measured thyroid activity content to the dose, bypassing the explicit assessment of the intake. The developed methodology of the thyroid dose assessment is an extension of approaches and the dose assessment technique prepared by the Ukrainian Radiation Protection Institute (RPI) within the project CAThyMARA, where only an acute intake and a single measurement were considered. In this work, the methodology has been extended to cower continues intakes, multiple measurements and other available information. The methodology introduces a concept of the ‘intake shape function’, which represents an individual-related relative intake rate. The function could be constructed on the base of environmental monitoring data, atmospheric transport modelling and individual history of residence and movements in the contaminated area. A method for the assessment of the thyroid dose due to intakes of a mixture of radioiodines and Te-132 is also proposed. It provides correction coefficients for assessed values of I-131/Te-132 doses and takes into account the age of the person, dominating route of intake and shape of intake function. Reference ‘dose per content’ functions were calculated with RPI biokinetic modelling tools and latest ICRP biokinetic and dosimetric models. These functions are a central part of the developed methodology and a pilot version of the smartphone-based data processing unit (DPU).
The pilot version of the DPU has been designed for the direct assessment of the absorbed thyroid dose and committed effective dose based on the post-emergency thyroid monitoring data in case of a severe nuclear accident. The DPU is a software for a smart device (Android smartphone or tablet) that permits the simple operation in conditions of an emergency after significant releases of radionuclides from a light water reactor.
The key input data required by the DPU are: results of a single measurement or time-series measurements of the I-131 and I-132 activity content in the thyroid gland; date and time of the nuclear accident/cease of the chain reaction; age/date of birth of the person or the gestational age of the foetus; time-course (shape) of the activity intake of I-131 and Te-132, associated with places visited by the exposed individual; information about the dominating route of intake (inhalation or ingestion) of radioiodines.
The output data of the DPU are: 30-day committed absorbed dose to the measured thyroid gland; committed absorbed dose to the thyroid gland of the foetus if maternal thyroid was measured; committed absorbed dose to the thyroid gland at the age 70 years; committed effective dose.
The ‘dose per content’ concept is the main technique used in this work for the reduction of uncertainties. The main advantage of the developed method is its simplicity and tolerance to the uncertainty/lack of information on characteristics of exposure conditions. The ‘dose per content’ function is mostly insensitive to the choice of inhaled particle sizes and chemical forms of inhaled radionuclides. The method involves all available data sources, such as Atmospheric Transport Modelling (ATM) and environmental monitoring data. Such a combination allows to focus the data harvesting on modifying factors with the highest impact and to reduce uncertainties on dose estimates associated with multiple intakes of different magnitude, unknown physical and chemical forms of the radioactive iodine, unknown levels of intake of short-lived radioiodines.
The developed methodology and the pilot version of the data processing unit permit fast thyroid dose assessments in nuclear emergencies. The mobile app for thyroid dose assessments allows offline collection, storage and processing of data for an unlimited number of exposed individuals and multiple measurements. The link of the developed data processing unit with thyroid measurement equipment and server applications will result in a cloud-based network of autonomous thyroid dose monitors for large-scale population screening in a nuclear or radiological emergency.
Wp2
Environmental Data
Intake Shape Function (IS)
Estimated Doses and Recommendations
ATM data
Intake Shape Function (IS) Constructor
Personal data
Passport data and other essential information
Locations and Routes
Measurement Data
Data Analysis
SERVER
Presentation and editing of measurement results
Dose assessment
Settings and reference information
Personal information
Investigated persons
Conceptual scheme of the smartphone-based data processing unit for assessment of the doses from intake of radioiodines and Te-132 on the base of thyroid monitoring data