## Slide 1
CONCERT Project Website (https://concert-h2020.eu)
CONFIDENCE Project Website (https://portal.iket.kit.edu/CONFIDENCE//)
NERIS Platform Website (https://www.eu-neris.net/projects.html)
External dosimetry using personal items
Alessia Mafodda, Clemens Woda, Jon Eakins
Institute of Radiation Medicine, Helmholtz Zentrum München , Munich, Germany
Centre for Radiation, Chemical and Environmental Hazards (CRCE), Public Health England, Chilton, England
alessia.mafodda@helmholtz-muenchen.de
2 - 5 December 2019
Lindner Hotel Gallery Central
Bratislava, Slovak Republic
CONFIDENCE Dissemination Workshop
“Coping with uncertainties for improved modelling and decision making in nuclear emergencies”
Introduction
Objectives
Materials and methods
Conclusion
Results
When a radiological accident occurs, a large-scale emergency might involve a great number of individuals.
The reconstruction of doses and related uncertainties to population is crucial to obtain a more consolidated picture of the radiological situation during the decision-making phase. Since people are not usually equipped with proper devices for ionizing radiation monitoring, everyday objects can eventually perform as fortuitous dosimeter.
Dosimetric properties of some personal items represent both valuable and challenging resource of information during an emergency scenario.
Optimization of measurement protocols using personal items such as electronic components (surface mounted resistor) from mobile phone circuit boards, memory cards and chip cards on the low dose-range (20-200 mGy) in case of accidental external exposure of gamma radiation.
Development of conversion factors to derive organ absorbed doses from the dose into the fortuitous dosimeters, for radionuclides and exposure conditions typical following major releases after a NPP accident.
RTL on resistors
For single resistors, measured with RTL technique, major sources of uncertainties in reconstructed doses are variation in intrinsic background signals (10-20 mGy), offset contribution of the calibration source (5 mGy) and variation in fading rates (20%).
MCNP simulations indicate that the overall systematic uncertainty, resulting from an unknown phone location on the body, when translating from phone dose to organ dose is around 20%.
External dosimetry using resistors from mobile phones in a potentially non-destructive approach could be possible with an uncertainty of 30-50%.
Reconstructing doses with memory cards was successful for doses of and above 2 Gy. Using the filler material to be able to measure low doses needs to be further investigated.
Wp2
OSL on memory cards and chip cards
MCNP simulations
Single Surface Mounted Resistor (1 mm x 0.5 mm) extracted from mobile phones circuit boards
New protocol for samples preparation
Readout using the Lexsyg Research luminescence reader: TL of Cr3+ emission at 695 nm
Memory cards from different producers:
Readout with OSL on intact cards and on the chemically extracted filler material using Risø TL/OSL-DA-15 and the Lexsyg Research additionally equipped with an emission spectrometry unit
Chip Cards from different type of cards:
Readout with OSL
ICRP Reference Male voxel phantom standing upon soil contaminated by a radionuclide (137Cs or 131I) wearing thin cylinders of pure aluminium oxide on four locations:
‘Chest’
‘Leg’
‘Back’
‘Hip’
RTL on resistors
OSL on memory cards
MCNP simulations
Dose recovery tests resulted in an overall overestimation in the low dose region (80, 60 and 40 mGy) (Example in Fig.1 - left). In fact, a strong zero-dose signal in the higher temperature range (320°) might contribute to the dosimetric signal (Fig.1 - right).
Chart: Glow curve - 40 mGy
Chart: DRT of 40 mGy
| 1 | 4 | 10 | 0
 | 1474 | 4633 | 10526 | -4
 | 3062 | 3062 | 0
Dose[mGy] | 53,09 ± 1,74
Fig.1
Trial irradiation with doses of 240 mGy ,100 mGy, 60 mGy, 40 mGy and 20 mGy (air kerma value) were performed on intact mobile phones affixed onto the ISO water slab phantom. Dose reconstruction was successful for all the values, and it was possible since signal is stable and can be easily corrected for fading. A fading rate study conducted on resistors sampled within one phone and between different phone models showed a fading rate of ∼20%.
137Cs | Conversion Factor, CPOL (Gy/Gy) |  |  | 
Location, L | Colon | Thyroid | Breast | RBM
Chest | 0.99 (0.03) | 0.84 (0.03) | 1.03 (0.03) | 0.90 (0.02)
Leg | 0.74 (0.02) | 0.63 (0.02) | 0.77 (0.02) | 0.68 (0.02)
Back | 0.81 (0.02) | 0.68 (0.02) | 0.84 (0.02) | 0.74 (0.02)
Hip | 0.82 (0.02) | 0.70 (0.02) | 0.86 (0.03) | 0.75 (0.02)
131I | Conversion Factor, CPOL (Gy/Gy) |  |  | 
Location, L | Colon | Thyroid | Breast | RBM
Chest | 0.93 (0.03) | 0.78 (0.02) | 0.98 (0.03) | 0.84 (0.02)
Leg | 0.71 (0.02) | 0.60 (0.02) | 0.75 (0.02) | 0.64 (0.02)
Back | 0.76 (0.02) | 0.64 (0.02) | 0.80 (0.02) | 0.69 (0.02)
Hip | 0.78 (0.02) | 0.66 (0.02) | 0.82 (0.02) | 0.70 (0.02)
The conversion factor, CPOL, from phone dose, DPL, to organ dose, DO, is obtained from the simple ratio:
CPOL = DO / DPL
where the superscript ‘L’ reminds that the value is dependent on the location of the phone.
Values for CPOL are provided for 137Cs in Table 1:
Table 1
Table 2
Values for CPOL are provided for 131I in Table 2:
Dose response of the OSL signal is linear up to at least 10 Gy (Fig. 2). The detection limit is estimated at 20-40 mGy. Fading is pronounced and leads to a signal loss of ~ 80% after 10 days. Consequently the detection limit increases to >100 mGy after this time.
In trial irradiations with memory cards placed inside a phone, doses of 2 and 5 Gy could be successfully reconstructed (within 25%), two to five days after irradiation, demonstrating that the material is in principal suitable as an external fortuitous dosimeter. For applications in nuclear emergencies, the sensitivity must be increased. This can be in principal achieved by chemically extracting the filler material (silica), which is the origin of the OSL signal.
Fig.2
Radionuclide source
Chest
Back
Hip
Leg
3 mm